## Slide 1: WF on whether gNB-DU is allowed to change PScell/PCell
Huawei, ZTE, Nokia, CATT, Ericsson,Samsung
3GPP TSG-RAN WG3 NR Ad-Hoc#1801 R3-170xxx
Sophia Antipolis, France, 22-26 January 2018

## Slide 2
Regarding the issue that whether gNB-DU is allowed to change PSCell/PCell, It is suggested to take way forward as the follows:
  PSCell/PCell can only be selected by the gNB-CU
  gNB-DU either accepts or rejects the PSCell/PCell requested by gNB-CU;
  A reject cause value, e.g. SpCell Failed To Be Setup, will be introduced if gNB-DU rejects the PSCell/PCell requested by gNB-CU.
  gNB-DU should provide assistance info to gNB-CU for further selection of PSCell/PCell, how to transfer assistance info for selecting PScell/PCell from gNB-DU to gNB-CU and which info to transfer e.g., cell load status, are FFS.