## Slide 1: Way Forward on n71 REFSENS configuration for 25 and 30 MHz
T-Mobile USA, Skyworks
3GPP TSG-RAN WG4 Meeting # 100-e R4-2114914
Electronic Meeting, Aug. 16-27, 2021

## Slide 2: Background
Uplink RB configurations for n71 20 and 30 MHz were proposed in R4-2112737
  All companies that commented in the first-round discussions supported the uplink configurations
REFSENS for n71 20 and 30 MHz also proposed in R4-2112737
  Several companies asked for more time to study the proposed values and gather additional data

## Slide 3: Proposed Way Forward
Proposal 1: For 25MHz and 30MHz downlink CBW operation, it is agreed that UL CBW is restricted to 20MHz
Proposal 2: The uplink RB configurations for 25 and 30 MHz n71 REFSENS on the following page are agreed (We leave it up to proponent to adopt either of the table formats. The first table format was used in R4-2112737. The second table format is how the spec is moving in other Wis. )
Proposal 3: Interested companies are requested to bring additional REFSENS measurements and analysis for 25 and 30 MHz n71 to RAN4#101 based on the uplink configuration above.

## Slide 4: Uplink configuration for reference sensitivity
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz | Duplex Mode | 
n71 | 15 | 25 | 25 | 20 | 20 | NOTE 5 | NOTE 5 |  |  |  |  | FDD | 
 | 30 |  | 12 | 10 | 10 | NOTE 5 | NOTE 5 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  |  | 
NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the uplink transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1). NOTE 5: For this DL channel bandwidth, the UL configuration of the highest UL channel bandwidth specified in Table 5.3.6-1 and the default Tx-Rx frequency separation specified in Table 5.4.4-1 shall be used. |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz | Duplex Mode | 
n71 | 15 | 25 | 25 | 20 | 20 | 20 | 20 |  |  |  |  | FDD | 
 | 30 |  | 12 | 10 | 10 | 10 | 10 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  |  | 
NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the uplink transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1). |  |  |  |  |  |  |  |  |  |  |  |  |