## Slide 1: WF on solution for Scell dropping issue
Huawei, HiSilicon, []
R4-2114949
3GPP TSG-RAN WG4 #100-e
August 16 – 27, 2021
Electronic meeting

## Slide 2: Background
Scell dropping issue: For CA, it is observed that the UE would drop the power on cell with lower priority when the allocated power on cell with higher priority occupies all the power ability of the UE.
Possible resolutions applicable for both FR1 and FR2 is proposed in [1][2][3][4]
  ‘RAN4 only solution’ but changes to RAN2 specifications also needed; configured power limits for UL serving cells and MAC-CE for enabling/disabling limits

## Slide 3
WF
The observed field issue applies for both intra-band and inter band UL CA.
  FFS for FR2 inter band UL CA
To solve the issue, it is agreed to be handled from Rel-17:
  RAN1 and RAN2 shall be involved in the discussion and their spec impact should be considered
  LS should be sent to RAN1 to check their understanding of this low priority CC dropping issue and the possible spec impact
  The specific solution is FFS
The study on Scell dropping solution should cover both FR1 and FR2 CA.

## Slide 4
Reference
[1] R4-2112826, “Resolution of the Scell dropping (power reduction) problem”, Ericsson
[2] R4-2112811, “Introduction of power limits for serving cells of UL CA” (FR1), Ericsson
[3] R4-2112816, “Introduction of power limits for serving cells of UL CA” (FR2), Ericsson
[4] R4-2114551 “Delta Pcell parameter to solve SCell dropping issue”, Qualcomm
[5] R4-2112383, “Views on SCell dropping for UL CA”, Apple
[6] R4-2113890, “R16 discussion on SCC drop”, OPPO
[7] R4-2114468, “Adding new objective to Rel-17 FR1 WI to prevent scell dropping for CA”, Huawei, HiSilicon
[8] R4-2114727, “Email discussion summary for [100-e][127] NR_RF_FR1_enh_Part_1_HPUE_ULMIMO”, Huawei, HiSilicon