## Slide 1: SIB1 carrier bandwidth and UE-specific CHBW
Clarification of the BS and UE specifications
Attachment to R4-2300749
Ericsson
3GPP TSG-RAN WG4 Meeting #106
Athens, Greece, 27 February – 3 March 2023
R4-2300749

## Slide 2: Issues relevant for current Rel-16 deployments
How to locate a Rel-15/16 UE with limited CHBW (MHz) support within a wider cell-specific BS BW (MHz)?
  also an issue with a Rel-17 RedCap UEs within the said cell-specific BW
  significant restrictions if the UE specific CHBW must be on the 100k channel raster
What is the applicable default duplex spacing for UE-specific CHBW?
  do the UL and DL BWPs have to be a default duplex spacing?
Do the carrierBandwidth and BWP have to correspond to a UE channel bandwidth (its maximum transmission configuration)?
  appears that the consensus is “no”, at least for the BWP
Not clear from the specifications, the NW not aware

## Slide 3: 1. Locating a UE-specific CHBW
Key question: what is the “RF channel” in 5.4.2.1? The same text in 38.104 and 38.101-1/2:
  “The channel raster defines a subset of RF reference frequencies that can be used to identify the RF channel position in the uplink and downlink. The RF reference frequency for an RF channel maps to a resource element on the carrier. [in 5.4.2.2]”
For a serving cell
  a resource grid is defined per numerology and carrier (38.211)
  one resource grid per numerology and transmission direction (38.211), the size is the carrierBandwidth, same size for all antenna ports
  the carrierBandwidth is advertised in SIB1, the bandwidth of the carrier
It is a carrier advertised in SIB1 that has to be mapped on the channel raster for at least one numerology, the “RF channel” contains this carrier
the 100k raster for compatibility with LTE within and between spectrum blocks
the carrier bandwidth = BS transmission bandwidth configuration for the numerology

## Slide 4: Making it clear in the specs: the carrier (cell-specific) on the channel raster
The RF reference frequency (channel raster) for an “RF channel” maps to a resource element on the carrier in SIB1, indicated to the UE by the BS, the same change in both specifications:
the UE specific channel bandwidths (also RedCap) not necessarily on the channel raster

## Slide 5: UE specific channel bandwidth
Can be located with PRB granularity within the carrier resource grid (cell specific) by ServingCellConfig, the carrierBandwidth in this IE mapping uniquely to a UE CHBW in MHz
  it is not another carrier with different size (only one resource grid per numerology and transmission direction)
If restricted to the 100k channel raster, impossible to locate a UE channel bandwidth with an odd/even-sized maximum transmission bandwidth configuration within a wider carrier resource grid with an even/odd-sized carrierBandwidth (SIB1) for SCS = 15k (m*180 + 90 = n*100 has no solution for any integers)
  Example: for a 25 MHz cell-specific BW (133 PRB carrier), impossible to locate a RedCap UE CHBWs of 10 MHz or 20 MHz spanning the initial BWP anywhere within the carrier, no matter if RedCap-specific (needed for A) or common BWP for all UEs (B), 5 and 15 MHz (if supported) can be located but only with with 5 PRB granularity
If the BS CHBW (38.104) is different from the UE-specific CHBW (38.101-1), one cannot require that both are always on the 100k channel raster, the “RF-channel” in 5.4.2.2 is cell specific and indicated to the UE by the BS

## Slide 6: 2. Default duplex spacing
The default duplex spacing applies to the UE channel bandwidth (38.101-1) if variable duplex is not supported by the UE, for TDD assumed that the center frequency is the same for both UL and DL
Symmetric UL/DL UE-specific CHBWs separated by default duplex spacing except for HD-FDD RedCap UE (Rel-17), but not necessarily active BWP within these BWs, required changes in 5.4.4:

## Slide 7: 3. The carrierBandwidth and BWP size(s) corresponding to UE channel bandwidth(s)?
In the Reply LS to RAN2 on supported BW for initial BWP R4-1909883, RAN4 provided a general answer
Any BWP size within the carrier resource grid (SIB1) for the relevant numerology can be supported, also made clear that a BWP size can be configured even if not tested by RAN4
The carrierBandwidth (SIB1) the carrier resource grid in which the UE can be expected to be configured with a BWP, can take any value up to 273 PRB just like a BWP size
The carrierBandwidth (SIB1) and BWP size(s) do not have to correspond to UE channel bandwidth(s)

## Slide 8: Proposal
From Rel-15 clarify in the specifications that
  the channel raster for the “RF channel” maps to a carrier advertised in SIB1 (cell-specific), centred on the channel raster for at least one numerology (BS and UE specifications)
  symmetric UL/DL UE-specific CHBWs are separated by the default duplex spacing if variable duplex not supported, active BWPs within these do not have to be at default duplex spacing (UE specification)
from Rel-16, add the exceptional raster point added at RAN#99 also to the UE specification consistent with the above
from Rel-17 that the default duplex spacing does not apply for HD-FDD RedCap UEs (UE specification)
Not necessarily included in RAN4-specification but assumed: UE-specific CHBW, BWP sizes and the carrier bandwidth in SIB1 can be configured according to the RRC specification
  not all configurations are tested by RAN4/RAN5 specifications
This would give guidance in the RAN4 specification for configuration of UEs and reduce the risks of rejected RRC configurations and UE malfunction due to different interpretations of the specification

## Slide 9: Annex: CA spacing with UE-specific CHBW
The frequency spacing between channel raster points of the carrier resource grids should be adjusted such that the separations of configured UE specific bandwidths are less than or equal to the nominal CA spacing for CA configurations with these specific bandwidths to be contiguous
Example: a 10 MHz carrier CC1 adjacent to a 20 MHz carrier CC2 on a 100 kHz raster, each carrierBandwidth (SIB1) set to the maximum transmission bandwidth configuration of the corresponding channel bandwidth.
  The nominal CA spacing (1) for the 10 + 20 MHz combination is 14.7 MHz while the nominal CA channel spacing (2) for the 10 + 10 MHz combination with the UE-specific bandwidth is 9.9 MHz. Setting the carrier spacing between channel raster points to 14.7 MHz, the frequency separations between center sub-carriers for both bandwidth combinations 10 + 20 MHz and 10 + 10 MHz are less than or equal to the respective nominal
  If the 10 MHz UE-specific channel is configured at the upper part of the 20 MHz carrier, the 10 + 10 MHz combination would become non-contiguous
  A restriction to the 100k channel raster would imply a 5 PRB granularity, not possible to configure 5 and 15 MHz UE-specific CHBW