## Slide 1
Simultaneous Elevation Sampling: RRA-MAP System
Installation site: National Radio Research Agency, Korea
Frequency coverage: 24 – 30 GHz
Multiple probes: 84 probes with 4 degree spacing
  Each probe is dual-pol circular horn antenna
  Finer elevation sampling with a goniometer movement
Receiver-probe pairs
  Each probe antenna with followed by a receiver module
  Receiver modules simultaneously sample the fields
< System w/o absorber >
< Photographs of RRA-MAP System >

## Slide 2
Receiver module operation
  Simultaneous operation at a sync signal
  Digitized data is transmitted only to the next module
  Last module delivers to the control computer
Merits
  Simultaneous sampling in elevation
  Short RF lines (only between probe and receiver module)
  Easy maintenance by replacing faulty module
  Denser probe configuration possible
Simultaneous Elevation Sampling: RRA-MAP System
< probe-receiver modules >
< probe-receiver connection >
< inter-module connection >

## Slide 3
EIRP pattern & peak search
  Near-field sampling with a 4 degree spacing
  EIRP pattern using NFTF
  Peak search with a fine accuracy
  Source: R4-2218724, RAN4 #105 (Nov. 2022)
Future development
  More functionality added to the modules
  Zero-rotation system covering an entire sphere may be considered
 | IFF (CATR) | Observation 1 | Observation 2
Configuration | CATR | multi-probe NFTF switch matrix | multi-probe NFTF multi-receivers
time (minutes) | 825 | 250 | 41
Simultaneous Elevation Sampling: RRA-MAP System
[ R4-2218724, RAN4 #105 (Nov. 2022) ]