## Slide 1: Motivation on supporting Intra-band non-collocated EN-DC/NR-CA deployment in Release 20 (Type 3 UE for handheld)
3GPP TSG-RAN WG4 Meeting #116
Bengaluru, India, 25-29 August, 2025
R4-2509644
KDDI, NTT Docomo, SoftBank, KT, LG Uplus

## Slide 2: Justification : Spectrum point of view in Japan
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
Y
SoftBank
3400
3440
3480
3520
3560
3600
SoftBank
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation
Docomo
Docomo
KDDI
Docomo
KDDI
Rakuten
KDDI
Notes: In this slide, we’re sharing Japanese backgrounds from spectrum point of view. There were 2 backgrounds.
Firstly, regarding Co-existence issue with Satellite systems, Tx Ant. Co-location is not always available due to two different co-existence conditions.
Next, regarding timing issue of Spectrum allocation, C-band 2 blocks were allocated at different time. This eventually makes Tx Ant. Co-location cost- Inefficient.

## Slide 3: Justification : Spectrum point of view in Korea
Co-existence with other systems
Timing of Spectrum allocation
  The 2 blocks in C-band will be allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
Y
3400
3500
3600
Candidate#3
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
SK Telecom
Candidate#1
Candidate#2
KT
LG Uplus
Notes: Additionally, in this slide, we’re sharing Korean backgrounds from spectrum point of view.
There are both co-existence issue and timing issue on spectrum allocation same as Japan.

## Slide 4: Justification
In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.
In Release 18, FR1 inter-band non-contiguous EN-DC with overlapping or partially overlapping bands and FR1 intra-band non-contiguous NR-CA for 2-layer case (Type 2 UE for handheld) are developed.
In Release 19, Intra-band non-contiguous non-collocated EN-DC/NR-CA for 4-layer case (Type 4 UE for FWA) are developed currently.
On the other hand, the similar functionality target for Type 3 UE for handheld was postponed for the future release. From operators’ point of view, it is desirable to standardize some enhancements in Release 20.
  Intra-band non-contiguous non-collocated EN-DC/NR-CA
    Type 3 UE
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 5: Justification : Rel-20 potential enhancement area (table)
UE Type | CC# | Antenna / LNA |  | Mixer | Analog BB | #Rx | HW | [Power] imbalance | UE Device
1 | 1 | 4 shared |  | 4 shared | 4 shared | 4Rx | 0.9x | 6dB full range | Handheld
 | 2 |  |  |  |  | 4Rx |  |  | 
2 | 1 | 2 | 4 total | 2 | 2 | 2Rx | 1x | 25dB full range | Handheld
 | 2 | 2 |  | 2 | 2 | 2Rx |  |  | 
3a | 1 | 4 shared |  | 4 | 4 | 4Rx | 1.2x | [xx]dB partial range | Handheld
 | 2 |  |  | 2 | 2 | 2Rx |  |  | 
3b | 1 | 4 shared |  | 4 | 4 | 4Rx | 1.4x | [xx]dB partial range | Handheld
 | 2 |  |  | 4 | 4 | 4Rx |  |  | 
4a | 1 | 4 | 6 total | 4 | 4 | 4Rx | 1.5x | [25]dB full range | FWA
 | 2 | 2 |  | 2 | 2 | 2Rx |  |  | 
4b | 1 | 4 | 8 total | 4 | 4 | 4Rx | 2x | [25]dB full range | FWA
 | 2 | 4 |  | 4 | 4 | 4Rx |  |  | 
Type 3 UE is a remaining area.
Rel-20
Under discussion in Rel-19
Rel-18
Rel-16
Notes: And then, in this slide, we’re proposing Rel-19 potential enhancement area based on results of Rel-18 WI.
Firstly, Type 1 UE is legacy Rel-15 UE. We had an easy mistake in this slide. Next, Type 2 UE is developed in Rel-18.
And then, Rel-19 potential enhancement area will be Type 3 and Type 4 UEs.
Specifically, Type 4 UE should reuse Type 2 UE requirements for power imbalance on UE RF and MRTD/MTTD on RRM.

## Slide 6: Justification : Rel-20 potential enhancement area (figures)
Type 3 UE is a remaining area.
Type 2: 2x2/cc, Separated 4Rx Chain
eNB(cc#1)
gNB(cc#2)
Conditions bw. gNBs
MRTD (33us)
Power imbalance (25dB)
Deployment scenario
Non-collocated
Different antenna pattern
Handheld
2 Rx Chain
2 Rx Chain
Type 3: 4x4/cc, Shared 4Rx Chain
Conditions bw. gNBs
MRTD ([xx]us)
Power imbalance ([xx]dB)
Deployment scenario
Non-collocated
Different antenna pattern
4 Rx Chain
Type 4: 4x4/cc, Separated 6/8Rx Chain
Conditions bw. gNBs
MRTD ([33]us)
Power imbalance ([25]dB)
Deployment scenario
Non-collocated
Different antenna pattern
FWA
4 Rx Chain
4 Rx Chain
eNB(cc#1)
gNB(cc#2)
eNB(cc#1)
gNB(cc#2)
Rel-18
Power imbalance ≦[xx]dB
4L
4L
2L
2L
4L
4L
Rel-20
Power imbalance ≦25dB
Power imbalance ≦25dB
Handheld
Under discussion in Rel-19
Type 2 requirement will be reused.

## Slide 7: Reference) Type 1 UE
Type1: 4x4/cc, Shared 4Rx Chain
Conditions bw. gNBs
MRTD (3us)
PSD imbalance (6dB)
Deployment scenario
Collocated
Different antenna pattern
4 Rx Chain
eNB(cc#1)
gNB(cc#2)
Rel-16/17
PSD imbalance ≦6dB
4L
4L
Handheld

## Slide 8: Potential Objectives
Proposal
  Type 3 UE requirements assuming MRTD<CP and power imbalance < [xx] dB for handheld
    Without intended impacts on the network side
Assumption/Background
  Type 4 : UE and NW sides
    Type 2 requirements (Pwr imbalance:25dB, MRTD:33us) will be reused considering similar separated UE Rx chain.
  Type 3 : UE sides
    The LNA will be shared between 2CCs for Type 3. It means any gain change initiated by one CC will affect another CC. Then it is important that the timing between 2CCs is aligned to some extent.
      If MRTD<CP, no performance impact is expected. However, power imbalance might be almost same as Type 1.
      If MRTD>CP, the gain change due to one CC will impact the performance of another CC within the received symbol.
  Type 3 : NW sides
      If MRTD<CP and additionally TAE/MRTD is tightened, it will impact the network deployment.
      If MRTD>CP, there seems to be no solutions for NW to avoid impacts for UE performance now.
Notes: Finally, same as proposals proposed by RAN chair and RAN4 chair, we propose two aspects.
Firstly, consider Type 4 UE assuming MRTD>CP for FWA with reusing Type 2 requirements.
And then, not to include Type 3 in March’24, but also check it in Dec’24. Type 3 requirements assuming MRTD<CP without intended impacts on the NW side.

## Slide 9
Appendix

## Slide 10: MRTD/CP for Intra-band non-contiguous
Power Imbalance
MRTD/TAE
  MRTD = TAE + RF_propagation_time_difference
  TAE (intra-band non-contiguous CA) = 3 us
Power imbalance (dB) | Inter-site distance (m) | Propagation time difference (us)
6 | 65 | 0.22
10 | 99 | 0.33
15 | 168 | 0.56
20 | 283 | 0.94
25 | 479 | 1.6
Table 1: Mapping between power imbalance, Inter-site distance and propagation time difference.
CP Length
Correlation of Power imbalance/ISD/Propagation time difference/MRTD/TAE/CP Length
  Observation: If tightening TAE<3us, existing almost operators will need to restructure their BSs.
Power imbalance (dB) | ISD (m) | Propagation time difference (us) | MRTD (us)
6 | 65 | 0.22 | 0.22 + 3(TAE)
10 | 99 | 0.33 | 0.33 + 3(TAE)
15 | 168 | 0.56 | 0.56 + 3(TAE)
20 | 283 | 0.94 | 0.94 + 3(TAE)
25 | 479 | 1.6 | 1.6 + 3(TAE)
Table 3: Correlation of Power imbalance/ISD/Propagation time difference/MRTD/TAE/CP Length
TAE
SCS (kHz) | CP Length (us)
30 | 2.34
60 | 1.17
Table 2: SCS/CP Length for n77/n78
Correlation of Power imbalance/ISD/Propagation time difference/MRTD/TAE/CP Length (R4-2300133, KDDI)
  If RAN4 keep current TAE(3us), in case of 30kHz SCS when n77/n78, always MRTD>CP regardless of power imbalance and ΔRF_propagation.

## Slide 11: Example) WI Objectives
The core part of the work item includes:
Phase I:
  Study the feasibility to support non-co-located scenarios for both FR1 inter-band EN-DC with overlapping and FR1 intra-band NR-CA for 4-layer case with shared Rx-chains (Type 3 for handheld).
    Discuss and decide reference UE architecture considering the UE capability of 4-layer MIMO case for both EN-DC/NR-CA
    Investigate the tolerable [power] imbalance between carriers
    Investigate the required arrival time difference between CCs
    Evaluate the UE performance under the [power] imbalance and arrival time difference
    Work is limited to EN-DC/NR-CA for bands B42, n77/n78
    Investigate whether the [power] imbalance should be explicitly (e.g. as an RF requirement) or implicitly specified (e.g. through a demodulation performance test). Specify the [power] imbalance based on the outcome of the investigation.
    If any change in RAN1 or RAN2 spec is needed, it will be triggered by RAN4 LS
Phase Ⅱ:
  Phase Ⅱ work will get started after the feasibility in phase Ⅰ is confirmed
  Specify MRTD and MTTD requirements and other identified RRM requirement impact(s) (if any) in non-collocated deployment
  Specify additional UE RF requirement(s) except for the [power] imbalance (if any) in non-collocated deployment

## Slide 12: Example) WI Objectives
The performance part of the work item includes:
Phase Ⅱ:
  Phase Ⅱ work will get started after the feasibility in phase Ⅰ is confirmed
  Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
    Define PDSCH demodulation performance requirement based on the applicable MRTD and [power] imbalance values.

## Slide 13
EOF