## Slide 1: Motivation on introduction of new NR band for 1.5GHz Japanese allocation
3GPP TSG-RAN WG4 Meeting #117
Dallas, USA, Nov. 17-21, 2025
R4-2520309
KDDI, NTT DOCOMO, SoftBank

## Slide 2: Justification
In Rel-15, band n74(UL: 1427-1470 MHz, DL: 1475-1518 MHz) was standardized to aim for achieving an eco-system with wider frequency range, to accommodate demands of some MNOs from different regions/countries. The above frequency range is aligned to the result of WRC-15. Therefore, n11 and n21 having same frequency ranges as B11 and B21 were not standardized.
On the other hand, a technical complexity of n74 is found from UE implementation point of view. This is mainly because the 5MHz gap between UL/DL of n74 is too narrow as known well. Nowadays, no n74 UE products are still provided eventually.
Japanese MNO operating 1.5GHz frequency [1] are intending migrations from 4G LTE(B11/B21) to 5G NR, and also facing the above issue on any UE products for operating 1.5GHz NR band.
Reference: [1] https://www.tele.soumu.go.jp/resource/e/search/myuse/use0303/1400m.pdf
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 3: Frequency range
We propose a new NR band with narrower frequency range and assuming a single duplexer.
Existing NR band n74 with dual duplexer
New NR band with a single duplexer
UL : 43MHz
1427
1470
1475
1518
UL : 35MHz
1427.9
1462.9
DL : 35MHz
1475.9
1510.9
Gap: Only 5MHz
Expand Gap: up to 13MHz
SoftBank
KDDI
docomo
SoftBank
KDDI
docomo
DL : 43MHz
(B11:20MHz)
(B11:20MHz)
(B21:15MHz)
(B21:15MHz)
【Reference】
Notes: And then, in this slide, we’re proposing Rel-19 potential enhancement area based on results of Rel-18 WI.
Firstly, Type 1 UE is legacy Rel-15 UE. We had an easy mistake in this slide. Next, Type 2 UE is developed in Rel-18.
And then, Rel-19 potential enhancement area will be Type 3 and Type 4 UEs.
Specifically, Type 4 UE should reuse Type 2 UE requirements for power imbalance on UE RF and MRTD/MTTD on RRM.

## Slide 4: Potential Objectives
Proposal
  Specify a new NR FDD band for the Japanese 1.5GHz frequency allocation spanning 1427.9-1462.9 MHz for UL and 1475.9-1510.9 MHz for DL
Assumption/Requirement
  Channel BW/SCS (*based on B11/B21 and n74)
  Power Class: PC3 (23dBm)
  UE architecture assumption: Single duplexer
    UE support both the new NR band for 1.5GHz and B11/B21 with common single duplexer.
  Other requirements
    Reuse the RAN4 requirements of n74 as much as possible
SCS (kHz) | channel bandwidth (MHz) |  | 
15 | 5 | 10 | 15
30 |  | 10 | 15
60 |  | 10 | 15
Notes: Finally, same as proposals proposed by RAN chair and RAN4 chair, we propose two aspects.
Firstly, consider Type 4 UE assuming MRTD>CP for FWA with reusing Type 2 requirements.
And then, not to include Type 3 in March’24, but also check it in Dec’24. Type 3 requirements assuming MRTD<CP without intended impacts on the NW side.

## Slide 5
Appendix

## Slide 6: Example) WI Objectives
The objective of this work item is to:
Specify a new NR FDD operating band to include band numbering and core requirements for Japanese 1.5GHz allocation spanning 1427.9-1462.9 MHz for UL and 1475.9-1510.9 MHz for DL by considering that:
  Support the channel bandwidth and SCS as follows;
  The use of UE power class 3 (*23dBm).
  UE architecture assumption: Single duplexer
    UE support both the new NR band for 1.5GHz and B11/B21 with common single duplexer.
  Other UE RF/RRM requirements
    Reuse the RAN4 requirements of n74 as much as possible
SCS (kHz) | channel bandwidth (MHz) |  | 
15 | 5 | 10 | 15
30 |  | 10 | 15
60 |  | 10 | 15

## Slide 7
EOF