## Slide 1: Way forward for CA38 AMPR
Huawei, CMCC, Nokia
3GPP TSG-RAN WG4 Meeting #64 R4-124973
Qingdao, P. R. China, 13 – 17 August, 2012
Agenda Item: 6.5

## Slide 2: Background
Simulation results are available in the following contributions
  For contiguous RB allocation,
    R4-123935, Huawei
    R4-124660, Qualcomm
    R4-124337, Nokia
    R4-123803, ZTE
  For cluster transmissions
    R4-123935, Huawei
    R4-124345, Nokia

## Slide 3: Way forward: contiguous allocation
The A-MPR requirements for contiguous allocation in the following table are agreed, pending further cross check and final confirmation before Dec 2012.
100RB/100RB | RB_End | L_CRB [RBs] | A-MPR for QPSK and 16-QAM[dB]
 | [0 – 12] | >[0] | ≤ [5] dB
 | [13 – 79] | > [RB_End – 13] | ≤ [2] dB
 | [80 – 180] | >[60] | ≤ [6] dB
 | [181 – 199] | > [0] | ≤ [11] dB
75RB/75RB | [0 – 70] | >[ RB_end -10] | ≤ [2] dB
 | [71- 108] | > [60] | ≤ [5] dB
 | [109 – 140] | >[0] | ≤ [5] dB
 | [140 – 149] | ≤ [70] | ≤ [2] dB
 | [140 – 149] | >[70] | ≤ [6] dB

## Slide 4: Way forward: multiple cluster transmission
The following A-MPR requirements for multiple cluster transmission are agreed, pending further cross check and final confirmation before Dec 2012.
========================================
A-MPR = CEIL {MA, 0.5}
Where MA is defined as follows
MA = [-14.17 A + 16.50; 0 ≤ A < 0.60
-2.50 A + 9.50 ; 0.60 ≤ A ≤ 1]
Where A = NRB_alloc / NRB_agg.

## Slide 5: Way forward:
The corresponding simulation results will be added in TR36.830 for CA 38 in Annex A as informative sub-clauses after final cross-check and confirmation.