## Slide 1: WF on Pcell interruptions for deactived Scell measurements in shorter measCycleScell case
NSN, Nokia, Alcatel-Lucent
R4-136996
3GPP RAN4#69
Agenda 5.2.3

## Slide 2: Background
R4-136139/6140 is proposing allow Pcell interruption for both intra and inter-band deactivated Scell measurement in shorter measurement cycle case, e.g. including up to 1% probability of missed ACK/NACK for 320ms SCell measurement cycle, since rel.10.
The considerations and issues towards the proposal for clarification are listed in following pages. And a WF is provided.

## Slide 3: Issue to clarify – packet loss
The UE Pcell interruption occurrences are not visible for the BS. The packet loss is unexpected and not due to the channel condition.
Each interrupted TTI will impact 3 DL + 4 UL packets Tx for this UE.
UL grant
missed
Interrupted SF
ReTx due to ACK/NACK missing
ReTx due to ACK/NACK missing
Tx wasted
Tx wasted
PDCCH/PDSCH loss in SF
PUCCH/PUSCH loss in SF
4 UL packets
3 DL packets

## Slide 4: Issue to clarify – packet loss
Impact due to interruption =
  for this single CA UE: increased 1% loss rate for PUCCH or PUSCH, PDCCH, PDSCH (on top of the level in normal Demod requirements) + forced reTx + wasted Tx + wasted UL grant
  for capacity: may have some loss if with large amount of CA UE with deactivated Scell.
Is it enough to only verify the overall impact with 1% ACK/NACK loss?
Should we also check the accumulated error for Demod, especially for cell edge UEs ?

## Slide 5: Issues to clarify – OLLA&OLPC
The BS expects an error rate of the same level as specified in Demod requirements.
Then the additional 1% loss will double the OLLA and OL power control effect:
  increase UE UL power due to UL packet loss  Power consumption may not be really resolved
  adjust the DL and UL scheduling lower performance and low capacity, esp. UL capacity for cell edge UE.

## Slide 6: Issue to clarify– measurement accuracy
Current accuracy requirement of the deactivated Scell is referring to the intra-f absolute requirements and inter-f relative requirements.
However there is no test case to verify the UE accuracy requirements under the condition of UE autonomous interruption.

## Slide 7: Question to clarify—Multiple Scells
Multiple DL Scells will be introduced in the specification and the current specification would likely be used as a starting point.
With the Multiple DL Scell case the interruption and packet loss rate may be equally in each Pcell and activated cells– however that is depend on the UE structure which is not decided yet.
Considering multiple Scell configuration, it is needed to give better overall view of the impact from packet drops for all scenarios.

## Slide 8: WF Proposal
Encourage companies to provide more analysis on the listed open issues in RAN4#70.