## Slide 1: WF on solution for CA interruption due to deactivated SCell measurements in Rel-12
Nokia Networks, Nokia Corporation
R4-145047
TSG-RAN Working Group 4 (Radio) meeting #72
Dresden, Germany, 18 – 22 August, 2014

## Slide 2: Solution for further investigation
Network triggers the actions below for UE in case of deactivated SCell measurement:
  UE who needs PCell/activated SCell interruption will indicate need for “Visible interruption”.
    This indicator could be band combination specific or applicable to all band combinations.
  UE who needs PCell/activated SCell interruption will report ”Visible interruption length” it needs.
Network decides to configure the gaps for “Visible interruption”
  Length of the gaps will be according to the UE reported ”Visible interruption length”.
  Companies are encouraged to provide proposals for default values of ”Visible interruption length”, “Measurement Length” and “Visible interruption Repetition Period” at RAN4#72 meeting
    Starting point the same as for measurement cycle
    Those gaps can also be the existing gap pattern (gap Id#0 or Id#1)
Implication of early implementation of the above solution should be studied and LS should be sent to RAN2

## Slide 3: Reference
Contributions on interruption handling in Rel-12 by NTT DOCOMO (R4-143320, R4-143902)
VIL
ML
VIL
VIRP
ML: Measurement Length
VIL: Visible interruption length
VIRP: Visible interruption Repetition Period