## Slide 1: Way Forward on NAICS UE Initial Simulation Assumptions
Mediatek
3GPP TSG-RAN WG4 Meeting #72bis Singapore, 6th – 10th October, 2014
Agenda Item: 7.12
R4-146812

## Slide 2: Way Forward (1)
Check RAN4 Chairs notes for NAICS agreements for these simulations
Simulation assumptions presented here are used for initial company alignment into RAN4#73.
Further discussion will introduce a larger range of simulations and assumptions than presented here

## Slide 3: Way Forward (2)
Initial NAICS assistance information
  Serving cell PA: Use -3dB
  CellID: Same as in SI (0,6,1)
  PA: Signal the set {-6,-3,0}dB with -3dB being transmitted from interference cells
  PB: Set to 1 in all cells
  TM set: All agreed major TMs are signalled, i.e. TM2, TM3, TM4, TM9
  MBSFN configuration: not used
  Resource allocation: Set to 1 PRB pair
The test cases truly reflect the NAICS assistance information listed above.

## Slide 4: Way Forward (3)
PDSCH Start position
  MMSE-IRC is used for the maximum number of PDCCH symbols and NAICS performance for the remaining symbols
Performance results for dominant interferer:
  CRS RSRP based strongest interference selection is considered
Test | TMs | Type | MCS | Rank | Antenna Config. | Interf. Type | Colliding
1 | TM4/4/4 | TBD | MCS5/5/5 | Rank1/1/1 | 2x2 | Fixed | Colliding
2 | TM9/9/9 | TBD | MCS5/14/14 | Rank1/1/1 | 2x2 | Fixed | Non-colliding

## Slide 5: Way Forward (4)
Range of test cases include the following test coverage:
  MBMS subframes are not covered
  CSI-RS is not included
  CSI-RS is also included
    8 Res with 10ms periodicity
Interference model – high and medium INR ON/ON model
CFI in the serving cell – 3
BD granularity – 1 PRB pair
Serving cell allocation – 12 ie the BW used for alignment is 3MHz

## Slide 6: Way Forward (5)
Test | TMs | Type | MCS | Rank | Antenna Config. | Interf. Type | Colliding
3 | TM2/2/2 | TBD | MCS5/5/5 | Rank1/1/1 | 2x2 | Fixed | Colliding
4 | TM2/3/3 | TBD | MCS5/14/14 | Rank1/1/1 | 2x2 | Fixed | Non-colliding
5 | TM9/4/4 | TBD | MCS5/5/5 | Rank1/1/1 | 2x2 | Fixed | Non-colliding
Companies are welcome to submit additional simulations listed in the table below