## Slide 1: Way forward on Test design
Ericsson, Verizon
3GPP TSG-RAN WG4 Meeting #73 R4-147574
San Francisco, Ca, USA, 16th-20th Nov, 2014

## Slide 2: BACKGROUND
RAN 4 has started the discussion on the test plan to verify NAICS feature
Only limited agreements have been reached so far
This way forward provides the
  Capabilities to be supported in Rel-12 NAICS
  Test scope
  The key aspects which should be included in the test plan/scope

## Slide 3: Capabilities
What is NAICS ?
  PDSCH IC (3 layers) + CRS-IC
  Blind detection
  Fallback capability
Carrier aggregation is supported together with NAICS capability.
  UE indicates the maximum number of carriers simultaneously supported by NAICS
  This is band/band combination independent to avoid penalization of certain operators/operators‘s combinations.
4 CRS AP is supported by the UE under Rel-12 NAICS via a capability signalling (as defined in RAN 1)

## Slide 4: Test scope
The test plan should reflect the NAICS capabilities:
  The following should be tested
    The capability of the UE to achieve gains when proper blind detection of the parameters is done in several conditions
    The capability of the UE to fallback to LMMSE-IRC in any conditions (unfavorable conditions and non-ideal backhaul).
    The capability of the UE to perform both PDSCH-IC and CRS-IC
  In addition
    4CRS AP support should be include in the test plan.
    CA support should be include in the test plan.

## Slide 5: Key aspects to capture in the test design
Randomization of the interference shall be used to test the BD capability of the UE
PDCCH shall be explicitly modeled in the test set
NAICS signaling shall represent the worst case (e.g. full set of TM, 1PRB case, maxnoofPA = 3)
Fallback performance shall be guaranteed
  Inaccurate signaling effect should be studied (PA, RA granularity) and potentially included in a test (signalling may not be up to date)
  Tests with unfavorable NAICS conditions should be included
CSI-RS configurations should be considered to reflect proper TM9 interference.
Time and frequency offsets should be considered to reflect practical interference.