## Slide 1: WF on CRS-IM demodulation (TM10)
Ericsson, Samsung, LGE
R4-151106
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 9th Feb – 13th Feb 2015

## Slide 2: For TM10
Generic CRS-IC is assumed as the reference receiver for TM10 operation.
For TM 10, non-colliding CRS is assumed, wherein the CRS between serving and dominant aggressor/interfering cell as well as CRS between dominant aggressor/interfering cells are assumed to be non-colliding.
For UE to support TM10, when TM10 is configured, not only the CRS explicitly indicated in the Rel-11 CRS assistance information can be cancelled, but also the CRS implicitly indicated in the COMP related signaling can be removed.
Consider DPS or DPB in the test setup for TM10.

## Slide 3: For TM10
For interference modelling, the following options can be considered as start point:
  Option 1: The interference modelling is derived based on the available results for homogeneous network.
  Option 2: Run new system level simulation for TM10 to extract the interference modelling
    The detail simulation assumption are given in the following slides.
  Other options are not excluded.
Interference modelling shall be prioritized in the next meeting

## Slide 4: Setup for option 2 (interference modelling extraction)
Both scenario 1 and scenario 3 are simulated
The CoMP system-level simulation assumptions given in section A.1 of 36.819 is reused for the system level simulation.

## Slide 5: Setup for option 2 (interference modelling extraction)
For alignments, the following options in section Table A.1-1 of A.1 of TR 36.819 is prioritized:
  Number of low power node per macro-cell: N=4
  Low power node TX power: 30 dBm
  System bandwidth: 10 MHz
  Possible transmission schemes in DL: DPS/DPB
  Number of antennas at transmission point: 2 for macro and 2 for low power node (base line)
  Number of antennas at UE: 2
  Antenna configuration: cross-polarized
  Antenna pattern: baseline configuration is taken
  Traffic model: non full buffer

## Slide 6: For TM10
Interested companies are encouraged to provide interference modelling in the next meeting
Interested companies are encouraged to provide link level simulation results based on the information given in R4-151107 and the given interference modelling in the next meeting.
  In R4-151107, the setup is just for information, any other options and changes are not precluded.
Interference modelling is prioritized over link level simulation