## Slide 1: Background of D2D interruption during ProSe Direct Commination
Intel
R4-151141
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 9-13 Feb, 2015
Agenda Item: 6.6.3.1

## Slide 2: Background(1)
Observation 1:
  If no interruption allowed during ProSe Direct Communication, D2D RX chain has to keep power on over an entire “saPeriod”.
  In ProSe Direct Communication, the percentage of null subframes, which do not carry any D2D data can be as large as 97.5% where there is only a single subframe carries data per 40ms.

## Slide 3: Background(2)
Observation 2:
  When SA reception is failed in a “saPeriod”, it is impossible to receive the consequent D2D data successfully.
  In this case, if no interruption allowed during ProSe Direct Communication, D2D RX chain has to keep power on over the majority of saPeriod with no D2D data being able to be detected.
As an example in the figure above, the power wastage can be quite high as (160-8)/160= 95%.