## Slide 1: Proposals and results on evaluation of CQI reporting for NAICS
Agenda Item: 6.6.2
Document for: Discussion
Source: Ericsson
3GPP TSG-RAN WG4 Meeting #74bis R4-151967
Rio, Brazil, 20th-24th April, 2015

## Slide 2: Principles for NAICS CQI reporting
The purpose of performance tests including demodulation and CSI shouldn’t be just for the sake of showing NAICS gain
  Test scenarios should be realistic to reflect the live network
By current CQI definition UE should have consistent behavior on the CQI reporting
  The network could optimize the system by trusting the reported CQI targeting at 10% BLER from each UE.
  The network has no knowledge if the UE has switched off NAICS receiver and fall back to IRC.
  The reported CQI should be independent on if the UE is scheduled with PDSCH or not
    Same CQI should be reported for the same interference
The CQI reporting method used from UE side should be feasible (complexity-wise) for all scenarios.
There should be enough CQI reporting gain to define proper CQI gain test.
  Note that the gain should come from the CQI reporting of a NAICS receiver but not from demodulation part

## Slide 3: RAN1 Agreement for NAICS CQI reporting
In Rel-12, there is no change to the current CQI definition for NAICS CSI reporting.
  The UE would take into account any NAICS gains in CQI derivation and it is up to RAN4 whether a new test case is required
    If RAN4 performance part does not find a feasibility of above note, this agreement do not preclude possibilities of RAN1 specification change

## Slide 4: Difference methods to be considered to present results
Different receivers with different CQI reporting methods
  IRC receiver on demod + IRC receiver on CQI
  NAICS receiver on demod + IRC receiver on CQI
  NAICS receiver on demod + CRS-IC+IRC receiver on CQI
  NAICS receiver on demod + Semi-static post NAICS receiver on CQI
  Other methods are not precluded
Dynamic post NAICS CQI reporting is considered to be not feasible from complexity of UE implementation under user cases when PDSCH is not scheduled
  Dynamic post NAICS CQI reporting is the only method matching to the RAN1 CQI definition to reflect any gain from demodulation

## Slide 5: Evaluation of gain of CQI reporting for NAICS
INR 80%@tile
EPA5 low
Fixed interference models
  Fixed model uses MCS=5 and RI=1 on NCs.
TM4/4/4, colliding CRS case with RI=1 in serving cell.
Follow CQI with wideband CQI reporting, follow PMI on serving cell
Results in terms of tput vs SINR
  Targeted SINR should be above >-3dB
  Averaged reported CQI statistic could be collected and presented
  BLER should be collected and presented
100%, 50%, 0% load on serving cell should be evaluated
  Partial and zero load on SC is with purpose to ensure consistent UE behavior on CQI reporting

## Slide 6: Evaluation of robustness of CQI reporting for NAICS
INR 20%@tile
EPA5 low
Fixed interference models
  Fixed model uses MCS=25 and RI=2 on NCs.
TM2/9/9, non colliding CRS case with RI=1 in serving cell.
Follow CQI with wideband CQI reporting, follow PMI on serving cell
Results in terms of tput vs SINR
  Targeted SINR should be above >-3dB
  Averaged reported CQI statistic could be collected and presented
  BLER should be collected and presented
100%, 50%, 0% load on serving cell should be evaluated
  Partial and zero load on SC is with purpose to ensure consistent UE behavior on CQI reporting

## Slide 7: OLLA parameters
Companies are welcome to provide results with and without OLLA to evaluate the impact of OLLA on different CQI reporting methods
If OLLA is included, using
  NACK: ~0.2dB
  ACK: ~0.02dB
  Start value :
    0dB for NAICS receiver with post-NAICS CQI
      Dynamic post-NAICS CQI reporting
      Semi static post-NAICS CQI reporting
    Optimized for NAICS receiver with pre-NAICS CQI
    Optimized for IRC

## Slide 8: Results for gain tests with fixed model
TP with fixed interference model as QPSK rank 1 with SC full load on PDSCH.
  This is the case where dynamic post NAICS is feasible

## Slide 9: Averaged reported CQI with fixed model
Fixed model uses QPSK rank 1 with 100% and 0% PDSCH load on SC.
It’s important to ensure the averaged reported CQI is same under different SC PDSCH load.

## Slide 10: Observations for gain test
Fixed interference model with QPSK RI=1 is taken as the most gain case from demod test
Dynamic post-NAICS CQI reporting can achieve less than 1dB gain with follow CQI compared to pre-NAICS IRC CQI reporting without OLLA.
  It’s not enough gain to define a proper CQI gain test as the 1dB gain is less than 1 CQI step as 2dB even for the most gain case with QPSK RI=1 scenario
OLLA with pre-NAICS IRC CQI reporting could achieve the same system performance as OLLA with dynamic post-NAICS CQI reporting.

## Slide 11: Summary
LS from RAN4 to RAN1 is needed to update the CQI definition as dynamic post-NAICS CQI reporting is not feasible
Pre-NAICS CQI reporting based on MMSE-IRC receiver can achieve optimized system performance with OLLA.
No CQI gain test is needed as no sufficient CQI reporting gain is observed.
FFS for CQI robustness test with more simulation results needed.

## Slide 12: Annex on draft CR for CQI definition change in RAN1
Reference R1-143297
7.2.3 Channel Quality Indicator (CQI) definition
The CQI indices and their interpretations are given in Table 7.2.3-1.
Based on an unrestricted observation interval in time and frequency, the UE shall derive for each CQI value reported in uplink subframe n the highest CQI index between 1 and 15 in Table 7.2.3-1 which satisfies the following condition, or CQI index 0 if CQI index 1 does not satisfy the condition:
A single PDSCH transport block with a combination of modulation scheme and transport block size corresponding to the CQI index, and occupying a group of downlink physical resource blocks termed the CSI reference resource, could be received with a transport block error probability not exceeding 0.1 assuming that the interference on the PDSCH REs is as seen on the interference measurement resources.
For a UE in transmission mode 9 when parameter pmi-RI-Report is configured by higher layers, the UE shall derive the channel measurements for computing the CQI value reported in uplink subframe n based on only the Channel-State Information (CSI) reference signals (CSI-RS) defined in [3] for which the UE is configured to assume non-zero power for the CSI-RS. For a UE in transmission mode 9 when the parameter pmi-RI-Report is not configured by higher layers or in transmission modes 1-8 the UE shall derive the channel measurements for computing CQI based on CRS.
For a UE in transmission modes 1-9, the UE shall derive the interference measurements for computing the CQI value reported in uplink subframe n based on only the serving cell CRS REs assuming that the interference is of unspecified origin with possibly no relation to other transmitted signals.