## Slide 1: WF on NAICS CQI Reporting
Qualcomm, Huawei, NTT DOCOMO, MediaTek, CMCC,…..
3GPP TSG RAN WG4 #74bis
Rio de Janeiro, Brazil, 20th – 24th April 2015
Agenda item 6.6.2
R4-152374

## Slide 2: NAICS CSI Reporting
RAN4 considers the performance and complexity of CQI reporting algorithms for NAICS CQI reporting
  Complexity of MMSE-IRC based CQI reporting is feasible for CQI reporting
  RAN4 acknowledges that, in some scenarios, the MMSE-IRC based CQI may under-report the CQI compared to NAICS demod BLER
RAN4 has determined that MMSE-IRC based CQI reporting is allowed for Rel-12 NAICS

## Slide 3: CQI Testing in RAN4
CQI test case(s) to be defined to ensure the following
(1) CQI robustness: CQI tested by RAN4 preserves NAICS demodulation gains compared to MMSE-IRC based demodulation
(2) CQI minimum gain: The performance of NAICS demod with the tested CQI is at least as good as MMSE-IRC based CQI reporting

## Slide 4: Concept of CQI Robustness
Step 1: Use a structured interference (Prior agreed randomized model comprising R1/R2 & 4/16/64 QAM) with HIGH and LOW INRs
  HIGH: INR1 = 13.91 dB, INR2 = 3.34 dB
  LOW: INR1 = 3.28 dB, INR2 = 0.74 dB
  With follow CQI, this yields a throughput of T1
Step 2: Use unstructured Gaussian interference of the same INR as above
  With follow CQI, this yields a throughput of T2
Step 3: Check Gamma = T1/T2 versus minimum requirements
  Gamma = [1] ensures NAICS robustness compared to MMSE-IRC demodulation (LOW INR)
  Gamma = [X], with X > 1, ensures that CQI reporting preserves NAICS demodulation gain (HIGH INR)
    Minimum requirement set based on assumption of MMSE-IRC CQI report
Details of simulation assumptions may be discussed further - to be finalized in RAN4 reflector by May 08th.