## Slide 1: WF on single D2D link demodulation performance requirements
Qualcomm Incorporated, LGE, Ericsson, Huawei, HiSilicon, Intel, Samsung
R4-153684
3GPP TSG-RAN WG4 Meeting #75
Fukuoka, Japan, 25-29 May, 2015
Agenda Item: 6.5.2

## Slide 2: Background
Following agreements were reached on single D2D link demodulation performance
This WF proposes the test and simulation setup for the single D2D link requirements
Category 1 | Single D2D link performance test
Test Purpose | To verify single link BLER-SNR performance in typical conditions
Required | Yes (agreed in R4 #74bis)
D2D channels | PSDCH, PSSCH, PSCCH, PSBCH
Fading | Yes
T/F offset | Yes
Discussion | 

## Slide 3: D2D Discovery
Test / Simulation Parameters |  | Test 1 | Test 2
Example applicable operating scenario |  | Intra-cell / Inter-cell synchronous | Inter-cell asynchronous
Rx pool synchronization window configuration |  | Not present | w1
# E-UTRA cells |  | 1 (serving cell, high SNR) FFS if neighboring cell is configured in the test | 
# D2D UEs |  | 1 | 2
D2D UE 1 | Transmission | PSDCH (0 ReTx)** | PSDCH (0 ReTx)**
 | Timing offset w.r.t. serving cell | +1us | +1us + 3.1ms
 | Freq offset w.r.t. serving cell | +200Hz | +300 Hz
D2D UE 2 | Transmission | not present | SLSS
 | Timing offset w.r.t. serving cell |  | +3.1ms
 | Freq offset w.r.t. serving cell |  | -100 Hz
Propagation Channel | Serving cell | [TBD]* | [TBD]*
 | D2D UE 1 | [EPA5] | [EPA5]
 | D2D UE 2 | - | [EPA5]
Channel BWs |  | 5 MHz | 
Rx UE assumptions (for simulation)*** | Timing reference | Serving cell | SLSS (from D2D UE 2)
 | Timing offset assumption (w.r.t. reference) | [-CP/2 CP/2] | [-CP/2 CP/2]
 | Frequency reference | Serving cell | 
Simulation results needed |  | PSDCH BLER | 
* AWGN is the baseline for simulations. Companies can analyze the impact of fading channel for serving cell.
** Does not preclude soft combining for Discovery. Companies can provide results with PSDCH retransmissions and soft combining.
*** For simulation purpose only; Does not preclude other UE implementations in practice.

## Slide 4: D2D Communications
Test / Simulation Parameters |  | Test 1 | Test 2 | Test 3
Example applicable operating scenario |  | Intra-cell / Inter-cell synchronous | Inter-cell asynchronous | OOC
SL-syncConfig configured |  | One Rx Pool; Sync config not present | One Neighbor cell Rx Pool; Sync config present | One Rx Pool
# E-UTRA cells |  | 1 (serving cell – high SNR); FFS if neighboring cell is configured in the test |  | 0
# D2D UEs |  | 1 | 2 | 2
D2D UE 1 | Transmission | PSCCH+PSSCH | PSCCH+PSSCH | PSCCH+PSSCH
 | PSSCH RMC | Option 1: 16QAM, TCR 1/2, [10 PRB pairs] Option 2: 16QAM, TCR 1/2, full BW allocation Option 3: QPSK, TCR 1/3, [10 PRB pairs] |  | 
 | Timing offset | +1us* (w.r.t. serving cell) | -1us + 10.1ms (w.r.t. serving cell) | +1us (w.r.t. D2D UE 2)
 | Freq offset | +200Hz (w.r.t. serving cell) | +300 Hz (w.r.t. serving cell) | +200 Hz (w.r.t. D2D UE 2)
 | TA in PSCCH | TA = 2 * CP | TA = 0 | TA = 0
D2D UE 2 | Transmission | not present | SLSS+PSBCH | SLSS+PSBCH
 | Timing offset |  | +10.1ms (w.r.t. serving cell) | (N/A - reference)
 | Freq offset |  | -100 Hz (w.r.t. serving cell) | (N/A - reference)
Propagation Channel | Serving cell | [TBD]** | [TBD]** | (not present)
 | D2D UE 1 | EVA70*** | EVA70 | EVA70
 | D2D UE 2 | - | EPA5 | EPA5
Channel BWs |  | 5 MHz / 10 MHz |  | 
Rx UE assumptions (for simulation)**** | Timing reference | Serving cell | SLSS (from D2D UE 2) | SLSS (from D2D UE2)
 | Timing offset assumption (w.r.t. reference) | [-CP/2 CP/2] | [-CP/2 CP/2] | [-CP/2 CP/2]
 | Frequency reference | Serving cell |  | SLSS (from D2D UE2)
Simulation results needed |  | PSCCH /PSSCH BLER | PSCCH / PSSCH BLER | PSCCH/PSSCH/PSBCH BLER
* +1us for simulations. Companies can evaluate the impact and possibility of +1us or -1 us, and decide in the next meeting.
** AWGN is the baseline for simulations. Companies can analyze the impact of fading channel for serving cell.
*** Companies can bring further results with high Doppler spread for Test 1, e.g., EVA300
**** For simulation purpose only; Does not preclude other UE implementations in practice.