## Slide 1: Way Forward on TRP/TRS discussion
Source： NTT DOCOMO, Intel Corporation, Nokia Networks, SGS Wireless
Agenda Item: 7.1.1
Document for: Approval
3GPP TSG-RAN WG4 #75 R4-153731
Fukuoka, Japan, 25th – 29th, May 2015

## Slide 2: Background
In the past several meetings, UMTS TRP/TRS for BHH and LEE have been discussed.
LTE requirement and some types of device are remained without discussion. Below table is referred to GCF LS(R4-146601) extracting only high priority test item.
Considering time limit of the WI (Dec. 2015), it seems to be difficult to finalize on due time the discussion for all type of the devices.
One of the reasons is that RAN4 does not have a framework for defining OTA TRP/TRS requirements.
Test Methods and Limits (both normative with pass/fail criteria and recommended) | RAT | Priority | Test Requirement | Situation in 3GPP
For handheld devices supporting voice and width < 72 mm | E-UTRA | 1 | Talk mode BHHR/L Browsing mode HR/L | Both are not discussed
For handheld devices supporting voice and width < 72 mm | UTRA | 1 | Talk mode BHHR/L Browsing mode HR/L | BHH is under discussion Browsing is not discussed
For data-centric devices | E-UTRA | 1 | Free Space measurements for Notebook LEE and Tablet LEE Free Space measurements (with ground plane phantom) for LME In addition, GCF requires RAN4 to develop a Test Specification or guideline for generic data centric devices, e.g.M2M device, SD Card Modem, etc. | UMTS: Notebook LEE is Fin.. LME and Tablet LEE are not discussed. LTE: all of them are not discussed.
For data-centric devices | UTRA | 1 |  | 

## Slide 3: Way forward 1/3
OTA TRP/TRS requirements are derived from measurements of real and commercial devices. No estimations, and no prototypes.
For a given frequency band, data should be comprised of measurements of devices intended for different markets where such given frequency band is considered roaming and also data for markets where that band is considered as Core. Data sets should be homogeneous in terms of support or not of CA. Nonetheless, data is contribution driven.
Interested companies share their measurements data through normal RAN4 contributions at least in form of a CDF. Companies also share CDFs via the TRP/TRS reflector, e.g. in Excel format.
For a given frequency band and test setup, the available data set CDFs shall be merged in a single overall RAN4 CDF for TRP and for TRS:
  The baseline for merging CDFs of data sets is described in R4-150907. Further improvements of the baseline can be discussed at RAN4#75-OTA-TRP/TRS-AH, considering e.g. the following topics: population size of data sets, merging of different data set CDFs.
OTA TRP/TRS requirements are defined as described below:

## Slide 4: Way forward 2/3
The following percentiles shall be picked from the overall RAN4 CDF:
  For TRP: [10th], [15th], [20th] percentiles of the CDF of TRP
  For TRS: [80th], [85th], [90th] percentiles of the CDF of TRS
If the distribution includes devices exhibiting significantly poor performance the following can be made:
  Option 1: A proper selection of the percentile above can ensure an appropriate failing rate for the performance requirement
  Option 2: Remove significantly poor performance devices from original data set CDF and update the merged overall RAN4 CDF.
Candidate values of TRP and TRS limits will be defined considering percentiles above.
Final requirement values of TRP and TRS will be defined offsetting candidate values according the comparison of standard deviation of overall RAN4 CDF and standard deviation of MU budget for the considered test setup. Baseline is in R4-150907. Further improvements can be discussed at RAN4#75-OTA-TRP/TRS-AH.
OTA TRP/TRS requirements are defined as described below (cont’d):

## Slide 5: Way forward 3/3
For TRP, the minimum of the minimum requirement is [TBD] dB below the avg.
For TRS, the maximum of the minimum requirement is [TBD] dB above the avg.
For TRP, the recommended value is 3 dB above the minimum avg. requirement
For TRS, the recommended value is 3 dB below the minimum avg. requirement
At RAN4#75-OTA-TRP/TRS-AH further discussions can address: percentile values, deltas between min/max and minimum requirement, deltas between minimum and recommended. Further, a methodology for deriving deltas above is not precluded.
At RAN4#75-OTA-TRP/TRS-AH primary focus is to finalize the framework
Framework will be first applied to UTRA BHH requirements
Proposal Schedule for encouraging contributions:
  UMTS test results of tablet LEE are called for by RAN4#75-OTA-TRP/TRS AH in July.
  LTE test results of notebook LEE are called for by RAN4#75-OTA-TRP/TRS AH in July.
  LTE test results of BHH and tablet LEE are called for by RAN4#76 and RAN4#76bis.
OTA TRP/TRS requirements are defined as described below (cont’d):