## Slide 1: WF for range of angle on OTA sensitivity
NTT DOCOMO,INC.
3GPP TSG-RAN WG4 Meeting #75 R4-153771
Fukuoka, Japan, 25th – 29th May, 2015 Agenda 7.2.3

## Slide 2: Background
The WF [1] on OTA sensitivity requirement was agreed in RAN4#74.
According to the WF[1] and on-line/off-line discussion in RAN4#75, agreement for the core requirement and WF on cell-specific OTA sensitivity are shown in following slides.

## Slide 3: Agreements in RAN4#75
There is a need to be able to describe an area (set of directions) within which an RoAoA can be positioned maintaining the declared EIS.
  This is the same thing as an area (set of directions) within which EIS can be achieved, although may not simultaneously over the whole area
# “RoAoA” is defined as a subset of the declared set of directions in this contribution, where the requirement is supposed to be met simultaneously.
(Example is shown in slide 7)

## Slide 4: Agreements in RAN4#75 (for core requirement)
  As the core requirement,
    OTA sensitivity requirement shall be met at the declared the set of directions. This declared set of directions is not specified, and the requirement may not be satisfied simultaneously over the whole declared set of directions.
  Vender shall declare
    the set of directions for which the OTA sensitivity requirement can be met (but may not simultaneously over the whole area)
# “RoAoA” is defined as a subset of the declared set of directions in this contribution, where the requirement is supposed to be met simultaneously.
(Example is shown in slide 7)

## Slide 5: WF(1/2)
  Clarification of the relationship between the conducted sensitivity and OTA sensitivity is FFS
  Whether it is necessary to declare or document anything about baseband functionality for the OTA sensitivity requirement is FFS
  How many points to test and what points to test is FFS (additional options are not excluded)
    Op1: 4 points (maximum/minimum theta direction with reference phi direction, and, maximum/minimum phi direction with reference theta direction)
    Op2: 5 points (4 points of Op1 and reference theta/phi direction)
# “RoAoA” is defined as a subset of the declared set of directions in this contribution, where the requirement is supposed to be met simultaneously.
(Example is shown in slide 7)

## Slide 6: WF(2/2)
  Additional vender declaration is FFS: candidate options are (additional options are not excluded)
    Op1: vendor declares EIS, a RoAoA (where RoAoA is constant in all position on the direction’s diagram)
    Op2: vendor declares EIS, four/five RoAoAs (where RoAoA varies in different position on the direction’s diagram)
# “RoAoA” is defined as a subset of the declared set of directions in this contribution, where the requirement is supposed to be met simultaneously.
(Example is shown in slide 7)

## Slide 7: Examples (2D steering case)
: the set of directions
[θ]
: Example RoAoA
[φ]
If the RoAoA
is optimized for this, outside of this RoAoA, OTA sensitivity requirement may not be met .

## Slide 8: Reference
[1] R4-151203, “Way forward on OTA sensitivity specification”, Nokia Networks