## Slide 1: WF for 4Rx PDSCH demodulation tests
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #75 R4-153829
Fukuoka, Japan, 25th – 29th May 2015

## Slide 2: Background
Proposals of PDSCH scenarios are provided by many companies.
  Summary of scenarios is given in the adhoc minutes and copied to next slide

## Slide 3: Summary of proposals for study
 |  | Ericsson (R4-153102) | Qualcomm (R4-152808) | Huawei (R4-152583) | LG (R4-153149) | Mediatek (R4-153195) | Intel (R4-153586)
TM1 | 8.2.1.1.1 | x |  |  | x | Reuse all IRC tests | 
TM2 | 8.2.1.2.1 |  | x | x | x |  | 
 | 8.2.1.2.2 |  |  |  |  |  | x
 | 8.2.1.2.4 | x | x |  |  |  | x
TM3 | 8.2.1.3.1 | x | x | x | x |  | 
 | 8.2.1.3.1C (Type C receiver) |  | IRC test? |  |  |  | x
TM4 | 8.2.1.4.1 |  | x | x | x |  | 
 | 8.2.1.4.1A | x | x |  |  |  | x
 | 8.2.1.4.2 | x |  |  | x |  | 
 | 8.2.1.4.3 |  | x | x |  |  | x
TM6 | 8.2.1.4.1B | x | x | x |  |  | x
TM9 | 8.3.1.1 |  | x | x | x |  | x
 | 8.3.1.1A | x | x |  |  |  | x
 | 8.3.1.2, +more layers | x | x | x | x |  | x

## Slide 4: WF for PDSCH demodulation tests
A goal is to align the set of test scenarios to be evaluated until RAN4#76
Evaluate the cases in the table on slide 5

## Slide 5: List of usecases to be studied
 | Based on | Receiver | Antenna configs | # of Layers |  | Options of Antenna correlations
TM2 | 8.2.1.2.1 Test 1 | MMSE | 2x4 |  | EVA5 | Medium / New Medium
 | 8.2.1.2.2 Test 1 | MMSE | 4x4 |  | EPA5 | Medium / New Medium
 | 8.2.1.2.4 Test 1 | MMSE –IRC | 2x4 |  | EVA70 | Low / New Medium
TM3 | 8.2.1.3.1 Test 1 | MMSE | 2x4 | 2 | EVA70 | Low / New Medium
 | 8.2.1.3.1C Test 1 (Type C receiver) | MMSE –IRC | 2x4 | 2 | EVA70 | Medium / New Medium
 | 8.2.1.3.2 | MMSE | 4x4 | 2 | EVA70 | Medium / New Medium
 | 8.2.1.3.1 Test 1 (2TX->4TX) | MMSE | 4x4 | 3,4 | EVA70 | Low
TM4 | 8.2.1.4.1 Test 1 | MMSE | 2x4 | 1 | EVA5 | Low / New Medium/High
 | 8.2.1.4.1A | MMSE | 4x4 | 1 | EVA5 | Low / New Medium/High
 | 8.2.1.4.2 Test 2 | MMSE | 2x4 | 2 | ETU70 | Low / New Medium
 | 8.2.1.4.3 | MMSE | 4x4 | 2 | EPA5 | Low / New Medium/High
 | 8.2.1.4.3 | MMSE | 4x4 | 3,4 | EPA5 | Low
TM6 | 8.2.1.4.1B | MMSE –IRC | 2x4 | 1 | EVA5 | New Medium /High
TM9 | 8.3.1.1 Test 1 | MMSE | 2x4 | 1 | EVA5 | Low / New Medium
 | 8.3.1.1A | MMSE –IRC | 4x4 | 1 | EVA5 | Low / New Medium
 | 8.3.1.2, | MMSE | 2x4 | 2 | ETU5 | Low / New Medium
 | 8.3.1.2 | MMSE | 4x4 | 3,4 | EPA5 | Low
This table and configurations are provided for simulation information.
Further modifications are not excluded.
The applicability of the usecases are based on the support by specifications