## Slide 1: WF on DL Control Channel IM Link-level simulation assumptions
Intel Corporation, ZTE
3GPP TSG-RAN WG4 Meeting #77 Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.4
R4-158136

## Slide 2: Way Forward (1)
This WF provides the set of link-level simulation assumption for the alignment simulations in the next RAN4 meeting
The following test cases are considered
# | Control channel | INR | Network Type | Duplexing | CRS pattern
1 | PDCCH / PCFICH | High Medium | Synchronous | FDD | Colliding
2 |  |  |  |  | Non-Colliding
3 | PHICH | High Medium | Synchronous | FDD | Colliding
4 |  |  |  |  | Non-Colliding
5 | EPDCCH | High Medium | Synchronous | FDD | Non-Colliding

## Slide 3: Way Forward (2)
The results are expected to be provided for the following reference receiver structures
  PDCCH/PCFICH and PHICH in synchronous networks
    LMMSE-MRC, LMMSE-IRC + CRS-IC, E-LMMSE-IRC, E-LMMSE-IRC + CRS-IC
  EPDCCH in synchronous networks
    LMMSE-MRC, LMMSE-IRC, LMMSE-IRC + CRS-IC
Notes:
  Companies should provide description of E-LMMSE-IRC receiver assumptions (e.g. granularity for covariance matrix estimation, assumptions on the interference control region duration)
  E-LMMSE-IRC results should be provided for different number of co-processed REs

## Slide 4: Common Simulation Assumptions
Parameters | Value
System bandwidth | 10MHz for both serving cell and interfering cells
Duplexing mode | FDD
Cyclic prefix | Normal
Number of interference cells | 2 interfering cells
Interference power profile | High INR: I1/Noc = 13.91 dB, I2/Noc = 3.34 dB Medium INR (I1/Noc = 7.77 dB, I2/Noc = 2.29 dB)
Network synchronization scenarios | Synchronous network Time offset: Interference cell #1 – 2us, Interference cell #2 – 3us Frequency offset: Interference cell #1 –200Hz, Interference cell #2 –300Hz
Cell ID | Serving cell: 0 Colliding CRS: Interferer cell #1 - 6, Interferer cell #2 - 1 Non-Colliding CRS: Interferer cell #1 - 1, Interferer cell #2 – 6
CRS ports | Port 0 and 1
Antenna configuration | 2x2 with Low correlation
Tx EVM | 6%
Unused Serving cell RE-s and PRB-s | OCNG

## Slide 5: PDCCH/PCFICH Simulation Assumptions
Parameters | Value
Scenarios | Scenario #1: Synchronous network + Colliding CRS Scenario #2: Synchronous network + Non-Colliding CRS
Channel model | Scenarios #1, 2: EPA5
Serving cell PDCCH | AL 2, 4; DCI Format 2 (43 bits – FDD, 10MHz)
CFI | Synchronous networks Option 1: CFIS = 1, CFII = 1 Option 2: CFIS = 3, CFII = 3
Number of PHICH groups (Ng) | 1
PHICH duration | Normal
Interference model for synchronous scenario | PDCCH/PHICH interference signals are emulated using random QPSK-modulated symbols with the SFBC-based precoding with per-REG signal transmission granularity: Scenario #1: 100% interference loading + Uniform power distribution Scenario #2: 50% interference loading + Non-uniform power distribution (random from -6dB to 6 dB) PCFICH interference is explicitly modelled PDSCH interference model is based on TM4 interference model B.5.3 in 36.101. - Probability of occurrence of transmission rank: rank 1:70% and rank2: 30% - Precoding granularity is 6 PRB
Performance metrics | Pm-dsg vs SINR

## Slide 6: PHICH Simulation Assumptions
Parameters | Value
Scenarios | Scenario #1: Synchronous network + Colliding CRS Scenario #2: Synchronous network + Non-Colliding CRS
Channel model | Scenarios #1, 2: EPA5
CFI | CFIS = 1, CFII = 1
Number of PHICH groups (Ng) | 1
PHICH duration | Normal
PHICH FRC | R.19 in TS 36.101
Interference model for synchronous scenario | PDCCH/PHICH interference signals are emulated using random QPSK-modulated symbols with the SFBC-based precoding with per-REG signal transmission granularity: Scenario #1: 100% interference loading + Uniform power distribution Scenario #2: 50% interference loading + Non-uniform power distribution (random from -6dB to 6 dB) PCFICH interference is explicitly modelled PDSCH interference is modelled as OCNG
Performance metrics | Pm-an vs SINR

## Slide 7: EPDCCH Simulation Assumptions
Parameters | Value
Scenarios | Scenario #1: Synchronous network + Non-Colliding CRS
Channel model | Scenario #1: EPA5
Serving cell EPDCCH | FRC #1: AL 2 Localized EPDCCH FRC #2: AL 4 Distributed EPDCCH DCI Format 2C (44 bits – FDD, 10MHz)
Number of PDCCH symbols and EPDCCH start | CFIS = CFII=2, EPDCCH starting symbols is derived from CFI
EPDCCH parameters | Number of EPDCCH Sets Configured = 1 Distributed EPDCCH set PRBs {3, 17, 31, 45} Localized EPDCCH set PRBs {0, 7, 14, 21, 28, 35, 42, 49} EPDCCH is transmitted in all subframes EPDCCH precoding model is in accordance to TS 36.101 B.4.4. and B.4.5
Interference model for synchronous scenario | Full PDCCH loading (OCNG) Partial loading PDSCH interference (PDSCH is transmitted in 50% of subframes) PDSCH interference is modelled as QPSK RI = 1
Performance metrics | Pm-dsg vs SINR