## Slide 1: WF on RRM impacts due to multi-carrier operation
Qualcomm Incorporated, Nokia Networks, Intel Corporation
R4-158139
3GPP TSG-RAN WG4 Meeting #77
Anaheim, CA, Nov 16th – Nov 20th, 2015

## Slide 2: Background
D2D requirements in Rel-12 were specified for the case of single CC operation
  when UE is configured only with PCell and D2D is on PCell, or
  when UE is out-of-coverage on all carriers and performing D2D using preconfigured resources (i.e. UE in any cell selection state)
In Rel-13 eD2D we are required to extend requirements to support multiCC operation
  UE can be configured with PCell and SCell(s).
  D2D operation can be on PCell, or SCell, or a non-serving cell.
  UE can be out-of-coverage on the ProSe carrier, while being associated with a serving cell on non-ProSe carrier

## Slide 3: Proposals
Proposal 1: RRM requirements for eD2D in TS 36.133 shall be extended to include all the supported multicarrier operating scenarios in Rel-13
Proposal 2: For D2D communications, existing requirements on interruptions shall be extended for PCell and activated SCell(s)
Proposal 3: For intra-frequency and inter-frequency D2D discovery reception, existing requirements on interruptions shall be extended for PCell and activated SCell(s); however, the exact amount of interruptions are FFS.
  FFS for interruptions allowed when discovery period less than 320ms
    Option 1: Same as specified for discovery periods greater than and equal to 320ms
    Option 2: Option 1 + additional upper limit of the interruptions
    Option 3: Only an upper limit of the interruptions
    Option 4: No interruptions allowed
    Other options are not precluded
Proposal 4: FFS if for inter-frequency discovery transmission on SCell/non-serving carrier, the UE is allowed 2 subframes interruption per discovery announcement/SLSS within a discovery period.
Proposal 5: RAN4 shall resolve the FFS in RAN4#78