## Slide 1: Way forward on coexistence evaluation methodology for NB-IOT in-band and guard band operation
Qualcomm, Huawei, Nokia Networks, ZTE, Intel, Ericsson, CMCC, NEC, CATT, NTT DOCOMO, INC
R4-158206

## Slide 2: Simulation assumptions
For NB-IOT and LTE simulation assumptions collected in R4-158207 should be used

## Slide 3: Simulation methodology
The simulation methodology for in-band and guard band scenarios consists of 3 steps:
  Computing the amount of power leakage:
    From NB-IOT to the N-th adjacent LTE PRBs.
    From LTE to NB-IoT.
    This step does not involve MonteCarlo simulation.
  Use system level MonteCarlo simulation to compute:
    the SINR distribution at n-th adjacent LTE PRB
    SINR distribution for NB-IoT users
  Determining the degradation:
    LTE throughput degradation due to NB-IOT
    NB-IoT degradation

## Slide 4: Step1: Computation of power leakage between NB-IOT and LTE
The power leakage between NB-IOT and LTE can be computed following the approach as follows:
  For DL simulation
    There is no need to perform this study
  For UL simulation
    For [3.75KHz] for single tone filtering needs to be considered
    For 15KHz for both single and multitones transmission, companies are encouraged to study the impact of the introduction on co-existence.
  The power leakage needs to be specified
    For LTE as victim, a function of n-th adjacent PRB
    For NB-IOT as victim, the granularity is per subcarrier spacing
  Filter assumptions:
    Refer to RAN1 agreement . In case, RAN1 does not have it, filter characteristic needs to be agreed by email discussion

## Slide 5: Step2: Computing the SINR
LTE PRB SINR and NB-IoT SINR distribution are obtained through MonteCarlo system level simulation methodology and power leakage computed in Step1

## Slide 6: Step3: computation of degradation
The computation of LTE throughput degradation, i.e. how to map PRB level SINR, to user level SINR is FFS
The computation of NB-IoT degradation (e.g. Outage) is FFS.