## Slide 1
3GPP TSG-RAN WG4 #78
ST. Julian, Malta, 15 – 19 Feb, 2016
Agenda item: 8.13.1
LG Electronics
WF on Adjacent channel coexistence evaluation for V2V service
R4-160511

## Slide 2: Objective
Define adjacent channel coexistence evaluations assumptions and methodology for 2GHz/5.9GHz V2V Services during 4 meeting times in RAN WG4. (restricted time limit to complete V2V Core requirements)
1) Up to 6GHz
Consider following interference scenarios
  V2V-to-Wifi/LAA/DSRC/V2V
  Wifi/LAA/DSRC/V2V-to-V2V
  1st priority is V2V-to-LAA and V2V-to-V2V Scenarios
  2nd priority is V2V-to-WiFi and V2V-to-DSRC Scenarios (if discussion time is allowed in WI)
  Reuse LAA deployment simulation parameters (RAN4 only consider DL transmission for LAA)
2) Licensed band (2GHz)
Consider following interference scenarios
  V2V-to-LTE/V2V
  LTE/V2V-to-V2V
  Both scenarios would be analyzed
  Reuse D2D deployment simulation parameters

## Slide 3: 1st Scenarios (Up to 6GHz)
Case 1 (aggressor-Victim)
  V2V UE-to-LAA UE
  V2V UE-to-V2V UE
Case 2 (aggressor-Victim)
  LAA BS-to-V2V UE
  Consider Band 46 for V2V service.
  Reuse LAA deployment simulation parameters.
LAA
V2V
f
V2V
f
V2V
V2V
LAA
f

## Slide 4: Deployment in up to 6GHz
Only consider outdoor deployment
Pathloss models
  V2V UE-to-LAA UE: follow V2P model defined in TR36.885
  V2V UE-to-V2V UE: follow V2V model defined in TR36.885
  LAA UE-to-V2V UE : follow P2V model defined in TR36.885
Used ACLR and ACS values for BS/UE LAA (20MHz)
  BS ACLR=35/38dB, BS ACS=43/46dB
  UE ACLR=30dB, UE ACS=27/30dB
Consider D2D ACLR and ACS values for V2V UE (10MHz)
  UE ACLR=30dB, UE ACS=33dB
  For power class 3 V2V UE, RAN4 consider 2 step ACLR requirements

## Slide 5: 2nd Scenarios in Licensed band (2GHz)
Case 3 (aggressor-Victim)
  V2V UE-to-LTE BS
  V2V UE-to-V2V UE
Case 4 (aggressor-Victim)
  LTE UE-to-V2V UE
  Consider V2V based on PC5 operation in licensed bands
  Reuse D2D deployment simulation parameters
LTE
V2V
f
V2V
f
V2V
V2V
LTE
f

## Slide 6: Deployment in Licensed Bands
Only consider outdoor deployment
Pathloss models
  V2V UE-to-LTE BS : follow the channel model between UE and macro eNB defined in TR 36.885
  V2V UE-to-V2V UE : follow V2V model defined in TR36.885
  LTE UE-to-V2V UE : follow P2V model defined in TR36.885
Used ACLR and ACS values for legacy LTE BS/UE (20MHz)
  BS ACLR=45dB, BS ACS=46dB
  UE ACLR=30dB, UE ACS=27dB
Consider D2D ACLR and ACS values for V2V UE (10MHz)
  UE ACLR=30dB, UE ACS=33dB
  For power class 3 V2V UE, RAN4 consider 2 step ACLR requirements

## Slide 7: Evaluation methodology
Static simulations
  Due to the restricted time units, RAN4 consider static simulations.
Evaluation metric
  Legacy system Throughput degradation due to adjacent channel interferer(s)
  For the V2V-to-V2V coexistence scenarios, reuse the LTE link-level curve or make new V2V link-level curve based on layer1 parameters. But need to more time for decision of RAN1.

## Slide 8: V2V simulation paramters
Deployment scenarios: Unban case
Simulation Block Size :
  Urban : 3*433m, 3* 250m (in page 9)
Absolute vehicle speed for urban (and Freeway)
  Urban : 15km/h, 60km/h
  Only reflected to decide vehicle density.
  Fixed location will be considered for adjacent coexistence evaluation.
  Vehicle density : Average inter-vehicle distance is 2.5 sec * absolute vehicle speed.
    E.g) Distance of V-to-V = 2.5 * 15km/h (4.167m/s) = 10.4 m
  V2V channel model : WINNER+B1 Manhattan grid layout model
  # of activate UEs per cell: Round (10% * # of total dropped UEs/cell)
  # of RBs : 50RBs / # of activate UEs per cell

## Slide 9: Deployment scenarios of urban case
ISD of eNB = 500m
For 2GHz, No deploy small cells
  # of LTE UE is 20 per macro cell
  UEs are dropped with the equal inter-UE distance in the middle of the sidewalk
For 5.9GHz, deploy 6 small cells on rooftop in each building
  # of LAA UE is 10 per small cell, no Macro cell
  UEs are dropped with the equal inter-UE distance in the middle of the sidewalk

## Slide 10: Way Forward [1]
Coexistence scenarios
  In 2GHz, consider V2V UE-to-LTE UE and V2V UE-to-V2V UE
  In 5.9GHz, consider V2V UE-to-LAA UE and V2V UE-to-V2V UE
    Only consider DL LAA operation in UE for coexistence analysis.
No needed to consider V2V UE mobility to verify the legacy ACS/ACLR requirement
Do not consider TDM operation for WAN and V2V in 2GHz FDD bands:
  Special operation : WAN and V2V operated in same operating band with TDM.
  However, other RAN WGs still discuss how to define the priority between WAN and V2V
General simulation parameters for licensed bands (2GHz) and LAA band (5.9GHz)
  Basic principle follows
    General deployment parameters in LAA WI for up to 6GHz
    General deployment parameters in D2D WI for 2GHz licensed bands

## Slide 11: Way Forward [2]
Detailed V2V communication parameters
  Follow detail parameters in V2V TR36.885 (RAN1) except mobility. E.g) Traffic model and deployment scenarios
  Focus on only Urban case : 15km/h and 60km/h
  V2V channel model : WINNER+B1 Manhattan grid layout model
  Number of activate UEs per cell: round (10%* total # of dropped UEs/cell)
    E.g) 15km/h case: [(2676/10.4)*14/21]*0.15 = [(257.3*14)/21]*0.15 = [3602.3 / 21]*0.1 = round (171.5 * 0.1) = 17
    E.g) 60km/h case: [(2676/41.7)*14/21]*0.15 = [(64.2*14)/21]*0.15 = [899.1/21]*0.1 = round (42.8*0.1) = 4
Detailed LTE/LAA UE dropping model
  For LTE coexistence analysis, Number of UE is 20 per macro cell
  For LAA coexistence analysis, deploy 6 small cells on rooftop in each building
    Number of LAA UE is 10 per small cell
  Number of activate UEs per cell : round (10%* total # of dropped UEs/cell)