## Slide 1: WF on BS demod performance for new PUCCH formats
Nokia Networks, Alcatel Lucent
R4-160522
3GPP TSG-RAN WG4 Meeting #78
St. Julian’s, Malta, 15 - 19 February 2016
Agenda Item: 6.14.1

## Slide 2: Proposals
BS demod performance requirements for PUCCH format 4 and 5 are defined in Rel-13. Same test setup is used for both PF4 and PF5.
BS demod performance requirements are defined as the SNR levels to achieve below CRC pass rate, regardless whether the message contents include HARQ-ACK, P-CSI, or both.
  99% in presence of signal, and
  1% in absence of signal if considered as necessary
The test case setup will correspond to the descriptive use cases of the new PUCCH formats with Rel-13 band combinations
  FDD and TDD: 24bits
    FDD: 4CC, 2bits for HARQ-ACK and 4bits for P-CSI per CC
    TDD: 2CC configuration 2, 8bits for HARQ-ACK and 4bits for P-CSI per CC
  TDD only: 48bits
    TDD: 4CC configuration 2, 8bits for HARQ-ACK and 4bits for P-CSI per CC
  Other assumptions for the performance tests are in the next slide
  Interested companies are encouraged to conduct simulations based on agreed assumptions and provide results for calibration in RAN4#78bis.

## Slide 3: Other simulation assumptions
Codeword selection | Random selection for both HARQ-ACK and P-CSI
Codebooks size determination | Semi-static
ACK repetitions | Disabled
Propagation conditions | EPA5, EVA70 Propagation channel definitions to be reused from 36.104.
Cyclic Prefix | Normal CP
Channel BWs | 10, 15, 20MHz
Carrier definition | Carrier frequency: 2.0 GHz PUCCH on PCell (single PUCCH group) Number of PRBs for PF4/5: 1
PUCCH multiplexing | 1 UE
Antenna’s configuration | UE: 1Tx BS: 2Rx, 4Rx, 8Rx correlation between branches is 0 no power imbalance between branches
Timing estimation | Perfect timing estimation
Frequency hopping | At slot boundary
DM RS frequency hopping | Disabled
Power control | Off