## Slide 1
3GPP TSG-RAN WG4 #78
ST. Julian, Malta, 15 – 19 Feb, 2016
Agenda item: 8.13.1
LG Electronics
WF on V2V coexistence simulation parameters
R4-161409

## Slide 2: Objective
Define adjacent channel coexistence simulation parameters for 2GHz/5.9GHz V2V Services during 4 meeting times in RAN WG4. (restricted time limit to complete V2V Core requirements)

## Slide 3: General paramters
Deployment scenarios: Unban case
Simulation Block Size :
  Urban : Manhattan grid model: 3*433m, 3* 250m (in page 6)
Absolute vehicle speed for urban
  Urban : 15km/h, 60km/h
  Used only to decide vehicle density.
  Fixed location will be considered for adjacent coexistence evaluation.
  Vehicle density : Follow TR36.885
  V2V channel model : Follow TR36.885
  # of activate UEs per V2V cell: Round (5% * # of total dropped UEs/cell)
  # of activate UEs per LTE/LAA cell : 3UEs

## Slide 4: Parameters in licensed band
Only consider outdoor deployment
Pathloss models
  V2V UE-to-LTE BS : Follow TR 36.885
  LTE UE-to-V2V UE : follow TR36.885 (P2V model)
Used ACLR and ACS values for legacy LTE BS/UE (10MHz)
  BS ACLR=45dB, BS ACS=46dB
  UE ACLR=30dB, UE ACS=27dB
Consider D2D ACLR and ACS values for V2V UE (10MHz)
  UE ACLR=30dB, UE ACS=33dB
  For power class 3 V2V UE, RAN4 consider 2 step ACLR requirements

## Slide 5: Parameters in unlicensed band
Only consider outdoor deployment
Pathloss models
  V2V UE-to-LAA UE: follow TR36.885 (V2P model)
  LAA BS-to-V2V UE : follow TR36.814 (ITU-R Umi)
Used ACLR and ACS values for BS/UE LAA (20MHz)
  BS ACLR=35/40dB
  UE ACLR=30dB, UE ACS=27dB
Consider D2D ACLR and ACS values for V2V UE (10MHz)
  UE ACLR=30dB, UE ACS=33dB
  For power class 3 V2V UE, RAN4 considers 2 step ACLR requirements
For optional test case, detailed parameters can be provided from interested companies.

## Slide 6: Deployment parameters of urban case
ISD of eNB = 500m
For 2GHz, No deploy small cells
  # of LTE UE is 20 per macro cell
  UEs are dropped with the equal inter-UE distance in the middle of the sidewalk
For 5.9GHz, deploy 6 small cells on rooftop in each building
  # of LAA UE is 10 per small cell, no Macro cell
  UEs are dropped with the equal inter-UE distance in the middle of the sidewalk

## Slide 7: Annex
Number of activate V2V UEs per cell: round (5%* total # of dropped UEs/cell)
  E.g) 15km/h case: [(2676/10.4)*14/21]*0.05 = [(257.3*14)/21]*0.05 = [3602.3 / 21]*0.05 = round (171.5 * 0.05) = 8
  E.g) 60km/h case: [(2676/41.7)*14/21]*0.05= [(64.2*14)/21]*0.05 = [899.1/21]*0.05 = round (42.8*0.05) = 2