## Slide 1: WF on eMTC demodulation and CSI
Huawei, HiSilicon, Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-162790
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Agreements
MPDCCH Precoder granularity
      Apply random precoding specified in TS36.101 B.4.4
        Pre-coder vectors are identical
          Within the repetition period in time domain
          Within 1 PRB in frequency domain
    One DC subcarrier puncturing is assumed in all MPDCCH, MPDSCH and CQI requirements
CRs for PBCH, MPDCCH CE Mode A, PDSCH TM6, CQI definition test are endorsed.
  Companies are encouraged to provide the ideal and practical simulation results in RAN4#79

## Slide 3: Common assumption for demodulation requirements
  UE frequency error modeling
    Option1: Practical UE frequency compensation
    Option2: Fixed UE frequency error
      CE Mode A: 50Hz
      CE Mode B: 100Hz
    Option3: Other UE frequency error model is not precluded

## Slide 4: Open issues for MDPCCH demodulation requirement
CE Mode A
  Number of repetitions
    Change 8 to 16 or 32 depending on whether the required SNR satisfies -6 dB
CE Mode B
  Propagation channel
    Three options: AWGN, ETU1, or EPA1
  Frequency hopping offset and MPDCCH Narrow band(i.e. first narrowband) while 4 narrowband used for frequency hopping
    option 1:
      Offset:1
      MPDCCH Narrowband:7
    option 2:
      Offset:2
      If 2 is set, need clarification of the behavior when MPDCCH is collided with PSS/SSS/PBCH
Notes: 7 8 1 2

## Slide 5: Open issues for PDSCH demodulation requirement
CE Mode A TM9
  SNR test point considering the sufficient MPDDCH decoding performance
    Option1: 0dB
    Option2: -6dB
    Option3: Other value is not precluded
  Coding rate
    Option1: 1/10 (TBS=152bits)
    Option2: 1/3
    Option3: Other coding rate is not precluded
  Number of repetitions
    Select the number which can satisfy the SNR test point

## Slide 6: Open issues for PDSCH demodulation requirement
CE Mode B TM2
  SNR test point to be set to -15dB
  Propagation channel
    Three options: AWGN, ETU1, or EPA1
  Number of repetitions:
    Option1: Number to satisfy BLER=30% with the target SNR with 1/3 QPSK
    Option2: Same or longer value than MPDCCH repetition.
      TBS size may need change

## Slide 7: CQI fading test with PUSCH 2-0
More studies are needed for the feasibility of the test metric.

## Slide 8: Simulation assumption
Refer to R4-161216 as baseline