## Slide 1: WF on BS demod performance for new PUCCH formats
Nokia, Huawei, NTT Docomo, Ericsson
R4-162802
3GPP TSG-RAN WG4 Meeting #78bis
San Jose del Cabo, Mexico, April 11 – 15, 2016
Agenda Item: 6.11.3

## Slide 2: Proposals
Use SNR to achieve 1% missed ACK rate as the performance metric for the BS demod requirements for new PUCCH formats.
BS demod requirements are defined based on following cases in Rel-13.
  PF4: 24bits payload with 1PRB
  PF4: 64bits payload with 2PRB as baseline, 3PRB for further consideration
  PF5: 24bits payload with 1PRB
  Reference receiver: with CRC, in case CRC check fail eNodeB considers all bits as “NACK”
  Assumptions for the performance tests are in the next slide.
  Interested companies are encouraged to provide simulation results with implementation margins for RAN4#79.

## Slide 3: simulation assumptions
Codeword selection | Random selection of HARQ-ACK
Codebooks | Semi-static (codebooksizeDetermination-r13=1)
ACK repetitions | Disabled
Propagation conditions | EPA5, EVA70 Propagation channel definitions to be reused from 36.104.
Cyclic Prefix | Normal CP
Channel BWs | 10, 15, 20MHz
Carrier definition | Carrier frequency: 2.0 GHz PUCCH on PCell (single PUCCH group)
PUCCH multiplexing | 1 UE
Antenna’s configuration | UE: 1Tx BS: 2Rx, 4Rx, 8Rx correlation between branches is 0 no power imbalance between branches
Timing estimation | Perfect timing estimation
Channel and Noise estimator | Practical
Frequency hopping | At slot boundary
Power control | Off