## Slide 1: Way forward on NB-IoT RLM
Huawei, HiSilicon, Qualcomm, Nokia, Ericsson, Intel, NTT DOCOMO, ZTE
R4-162872
3GPP TSG-RAN WG4 #78bis
San Jose Del Cabo, Mexico, 11 – 15 April, 2016
Agenda Item: 6.13.5

## Slide 2: Background
It has been agreed in RAN2 that RLM should be supported by NB-IoT UE
In last RAN4 #78 meeting, the following agreements on RLM were reached:
  RAN4 is to study RLM performance of NB-IoT UEs using following options:
    Option 1: Measurement based on NB-RS signals
      To be used as simulation baseline only.
    Option 2: Measurement based on synchronization signals (e.g. NB-SSS)
      provided that NB-SSS are available for measurement
    Option 3: Measurement based on combination of NB-RS and NB-SSS.
      provided that NB-SSS are available for measurement
    Other options are not precluded
  RAN4 is to study whether the existing RLM procedure can be reused for NB-IOT.

## Slide 3: Consensus
The existing framework of RLM requirement for Cat-M1 UE can be reused for NB-IoT RLM
The transmission parameters and evaluation periods should be revisited, based on the outcome of simulation results.
  Assuming hypothetical NPDCCH BLER thresholds of 2% and 10%
RAN4 is to study whether to specify different RLM requirements for different coverage modes.
Whether the same or different transmission parameters are needed for RLM when NB-UE is configured on anchor carrier or non-anchor carrier is FFS.
RAN4 is to further study whether to specify different RLM requirements for different operation mode (inband, guardband and standalone)
NB-RS based measurements is considered as baseline for UE configured on non-anchor carrier. It is FFS whether UE is to use NB-PSS/NB-SSS for measurement in addition to NB-RS for RLM on anchor carrier.