## Slide 1: 3GPP TSG-RAN WG4 Meeting #78bis San José Del Cabo, México, April 9th –17th, 2016
Intel, MediaTek
4RX SDR, CA Test
R4-163043

## Slide 2: Background
4-RX UE needs tests for CA support in Rel-13 as 2-RX UE.
4-RX UE test scopes :
  Sustain high data rate (SDR) tests with a single CC and CA
  CA throughput performance test
One concern is that 4-RX CA test structure is complex due to CA and 2/4-MIMO layer combinations.

## Slide 3: 4-RX SDR Test
Consider a new CA SDR test applicability rule for UE with mixed 2 layer and 4 layer support.
  Convert each of 4 layer CC to two 2 layer CCs. Number of CCs and aggregated bandwidth are changed increased by the conversion.
  Reuse existing CA SDR test applicability rule to select CA configuration/bandwidth combination.
Companies provide details of 4-RX SDR test setting in the next meeting.

## Slide 4: 4-RX CA Performance Test
4-RX CA Test configuration is based on 2-RX legacy Test.
Baseline RX for Rel-13 CA tests
  Option 1 : MMSE-MRC
  Option 2 : MMSE-IRC
Companies provide performance and test preference in the next meeting.

## Slide 5: Further Way-forward
Companies provide preference on 4-RX SDR, CA tests further way-forward.
Option 1 : Continue the ongoing Rel-13 WI to include 4Rx CA tests with minimum scope.
Option 2: Postpone the 4Rx CA tests for both normal demodulation tests and SDR tests into a new WI in next release. Rel-14 CA tests will be applied to Rel-13 UE release independent manner.