## Slide 1
3GPP TSG-RAN WG4 #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
Agenda item: 8.11.4
LG Electronics
WF on way to close V2V RRM core requirement timely
R4-165608

## Slide 2: Background
Completion of V2V Core requirement is Sept.2016.
Many issues have been discussing in RAN1 & RAN2 and some of them give impact on RAN4 requirements.
It seems to be difficult to close all V2V RRM core requirement timely.
New V2X WI was agreed in RAN#72
  V2X includes V2V, V2P and V2I/N.
  This work item should take into account the functionalities that are to be specified in the related work on sidelink V2V. This work item should also incorporate the important aspects that cannot be completed on time in V2V WI, if any, subject to decision by RAN plenary.
Based on the objective of V2X, it is possible to defer incomplete requirement of V2V to V2X.
To close V2V timely, prioritization of core requirements can be considered.
V2X is commonly represented for V2V, so all requirements can be expressed with V2X regarding forward specification.

## Slide 3: Way Forward
Following requirements deferred to V2X WI
  Requirements related to MCC operation & single carrier operating on E-UTRA
  Congestion control & collision avoidance
  Cell detection in Any Cell Selection State
  Interruption to WAN
Requirements out of 3GPP scope are not specified.
  Requirements requiring GNSS receiver performance
    Selection/Reselection to GNSS Sync Reference
    Initiation/Cease of GNSS based SLSS transmission

## Slide 4: Way Forward
Following requirements are specified in V2V WI
  Requirements related to a dedicated V2X carrier
  UE transmission timing
    eNB as time reference
    GNSS as time reference
    SyncRef UE as time reference
  Selection/Reselection of V2V Sync.Reference
    To SyncRef UE
  Initiation/Cease of SLSS transmission
    eNB based SLSS
    SyncRef based SLSS
  Measurement for selection/reselection
    With general context