## Slide 1: WF for A-MPR CBRS band
Nokia, Qualcomm Incorporated
R4-166920

## Slide 2: Background
A-MPR values for CBRS band was discussed in RAN4#80 and following text proposals were agreed for TR 36.744 [1][2].
[1] R4-165407, TP to TR36.744: A-MPR for 3.5 GHz in US, Nokia
[2] R4-166504, TP for TR 36.744: A-MPR for 3.5 GHz band in the US, Qualcomm Incorporated

## Slide 3: WF for A-MPR for CBRS band
CBW | RBstart | RBend | L_CRB | A-MPR
5 | – | – | – | 0 dB
10 | – | – | – | 0 dB
15 | 0 – 6 | – | ≤ 15 | ≤ 4 dB
 | – | 68 – 74 |  | 
 | ≥0 | – | ≥ 60 | ≤ 2 dB
20 | 0 – 12 | – | ≤ 20 | ≤ 4 dB
 | – | 87 – 99 |  | 
 | 13 – 15 | – | ≤ 3 | ≤ 1 dB
 | – | 84 – 86 |  | 
 | ≥0 | – | ≥ 60 | ≤ 3 dB
Based on discussions in RAN4#80 following A-MPR table is agreed for 3.5 GHz CBRS band in US.