## Slide 1: WF on MPR\AMPR simulation assumptions for UL 256QAM
Huawei, Hisilicon, Qualcomm, CMCC, Nokia, Skyworks, Ericsson []
3GPP TSG-RAN WG4 Meeting 80 R4-166954
Gothenburg, Sweden, 22 – 26 Aug, 2016

## Slide 2: Background
Simulation assumptions or results for MPR are provided by the following contributions
  R4-165476, EVM and ACLR Power Amplifier measurement with 256QAM, Skyworks Solutions Inc.
  R4-165702, Link simulation results for UL 256QAM, Ericsson
  R4-165195, UL256QAM TX challenges, Qualcomm
  R4-165408, UL 256-QAM MPR, Nokia
  R4-166117, Discussion on RF requirements for UL 256QAM, CMCC
  R4-163969, Simulation assumptions for MPR/A-MPR on UL 256QAM, Huawei, HiSilicon

## Slide 3: Background
MPR simulation assumptions based on EVM could be summarized as
EVM requirement | PA(%) | Transmitter(%) | Phase Noise (%) | I/Q image(%) | Total EVM(%)
Qualcomm | 1.5 | 1.34 | 1.78 | 2.24 | 3.5
Ericsson | [2.0~] | 1.03 | 1.78 | 2.0 | [3.5~]
Nokia | 1.93 | 1.06 | 1.78 | 2.07 | 3.5
Skyworks (option1) | 1.5 |  |  |  | 3.39
Skyworks (option2) | 2.0 |  |  |  | 3.64
CMCC | 2.0 | 1.03 | 1.78 | 2.0 | 3.5
Huawei | 2.0 | 1.03 | 1.78 | 2.0 | 3.5
Average | 1.85 | 1.1 | 1.78 | 2.06 | 3.47

## Slide 4: Background
Contribution R4-165408 shows in-band emission would be a limitation for MPR evaluation for UL 256QAM
This is not the intention of the in-band emission requirements

## Slide 5: WF on MPR assumptions->EVM
PA calibration point:
  UTRA_ACLR1 = 33 dBc, UTRA_ACLR2=36dBc, E-UTRA_ACLR=30dBc @ Pout = 22 dBm for 100RB QPSK signal
  Calculate MPR as total backoff needed for 256QAM from this calibration point. Final total reported MPR based on the calibration point will take into account the calibration waveform which is 1dB MPR 100RB waveform as described above
Single carrier C_IM3 = 60dB
2UL CA C_IM3 = FFS, C_IM5 = FFS
EVM requirement for each contributor could be summarized as following
Tx EVM contributor | EVM | SNR(dB)
PA | 1.85% | 34.7
Transmitter | 1.19% | 38.5
Phase noise | 1.78% | 35
IQ imbalance | 2.06% | 33.7
Total | 3.5% | 29.1

## Slide 6: WF on MPR assumptions->In-band emission
For UL 256QAM
  Opt1. Evaluate MPR by considering the legacy in-band emission requirement in 36.101
  Opt2. Evaluate impact of modified in-band emission requirement to MPR.
Companies are encouraged to provide more views on in-band emission issue for UL 256QAM in next meeting.