## Slide 1: Way Forward on Simulation Assumption and Methodology for the coexistence study between CDMA and NB-IoT
China Telecom, Samsung, Huawei, Qualcomm, Ericsson
3GPP TSG-RAN WG4 Meeting #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
Agenda Item: 9.3.1
Document for: Approval
R4-166994

## Slide 2: References
3GPP2 C.S0010-D V1.0, “Recommended Minimum Performance Standards for cdma2000 Spread Spectrum Base Stations”.
3GPP2 C.S0011-D V1.0, “Recommended Minimum Performance Standards for cdma2000 Spread Spectrum Mobile Stations”.
TR 36.802
TR 36.942
TR 25.942
Company Contributions:
[1] RP-151621, “New Work Item: NarrowBand IOT (NB-IOT)”, Qualcomm
[2] R4-165274, “Consideration on NB-IoT coexistence with CDMA”, China Telecom
[3] R4-165769, “Simulation Assumptions for NB-IoT Co-existence with CDMA”, Qualcomm
[4] R4-165931, “Discussion on General Coexistence Scenarios and Simulation Methodology”, Samsung
[5] R4-165932, “Discussion on CDMA2000 1x RF Performance”, Samsung
[6] R4-165933, “Discussion on Detailed Coexistence Simulation Assumptions and Parameters”, Samsung, China Telecom
[7] R4-166365, “Discussion on CDMA ACLR and ACS for co-existence simulation”, Huawei
[8] R4-166239, “NB-IoT and CDMA coexistence ”, Ericsson

## Slide 3: Interference scenarios
Standalone NB-IoT to coexistence with CDMA 1x should be evaluated in this study.
Cases | Aggressor system | Victim system | Link Direction | Deployment
1 | NB-IoT | CDMA1x | DL | Uncoordinated
2 | CDMA1x | NB-IoT | DL | Uncoordinated
3 | NB-IoT | CDMA1x | UL | Uncoordinated
4 | CDMA1x | NB-IoT | UL | Uncoordinated

## Slide 4: Evaluation Methodology
The evaluation methodology applied for coexistence study of NB-IoT system in TR36.802 is reused.
  Static system simulation
  The results should be presented as a function of ACS (when NB-IoT is victim) and as a function of ACLR (when NB-IoT is aggressor)
  Metrics and criteria for coexistence study
    For NB-IoT, SINR loss s less or equal to 1dB
    For CDMA , Capacity loss is less or equal to 5%

## Slide 5: General Simulation Assumption
Simulation parameters of Standalone NB-IoT for R13 coexistence study are reused.
Simulation parameters of CDMA 1x are mainly refer to TR25.942, while the CDMA1x BS and UE’s ACLR and ACS values are derived from 3GPP2 specs in C.S0010-D and C.S0011-D.

## Slide 6: Simulation Assumption
 | NB-IoT standalone | CDMA2000 1x
Carrier frequency in GHz | 0.85 | 0.85
Size of each nominal channel BW in MHz | 0.2 | 1.23
Transmission bandwidth in MHz | 0.18 | 1.23
Environment | Urban macro | Urban macro
Network layout | 19-sites [57 sectors] with wrap-around | 19-sites [57 sectors] with wrap-around
Inter-site distance in meter | 750m (Same for aggressor and victim) | 750m (Same for aggressor and victim)
System loading and activity | Full buffer 100% | All users with 9.6kbps speech
Network location | Non co-located (at cell edge of legacy) | Non co-located with IoT
DL subcarrier spacing | 15kHz | n/a
UL | See RP-152284 | n/a
DL power control | No | TR25.942 (reuse UMTS PC)
UL power control | 36.942 section 5.1.1.6 (set 1) by bandwidth scale, target SNR at BS is 15 dB | TR25.942 (reuse UMTS PC)

## Slide 7: Simulation Assumption
 | NB-IoT standalone | CDMA2000 1x
Frequency reuse | 1 | 1
Number of scheduled UE per cell (DL) | 1 | According to 95% users achieving target of (Eb/N0-0.5)dB; non orthogonality 0.2; target Eb/N0=5.5dB
Number of scheduled UE per cell (UL) | 3 for multi-tone (60kHz per UE), 12 for 15kHz single-tone, 48 for 3.75kHz single-tone | according to 5.5dB noise rise; target Eb/N0=4.0dB no MUD utilized, beta=0
BS antenna height in meter | 30 | 30
BS max TX power in dBm | 43/200kHz | 43
BS Tx power of common channel in dBm* | n/a | 36.5 (R4-030558 22.4% Total Power)
BS antenna gain including feeder loss in dBi | 15 | 15
BS antenna pattern | Horizontal (TR36.942) | Horizontal (65deg for -3dB)
BS antenna front-back ratio in dB | 20 | 20

## Slide 8: Simulation Assumption
 | NB-IoT standalone | CDMA2000 1x
UE antenna height in meter | 1.5 | 1.5
UE TX power in dBm | -40 to 23 | -52 to 23
UE antenna gain in dBi | 0 | 0
Building penetration loss | 45.820 Annex D.1 | n/a
Cell selection margin in dB | 3 | 3
BS-MS min couple loss in dB | 70 | 70
BS ACLR in dB | 40 to 60** | 37.2 (own channel measurement BW: 1.23MHz adjacent channel measurement BW: 180kHz)
BS ACS in dB | 40 to 50** | 71 (own channel measurement BW: 1.23MHz adjacent channel measurement BW: 180kHz)
UE ACLR in dB | 20 to 50** | 34.2 (own channel measurement BW: 1.23MHz adjacent channel measurement BW: 180kHz)
UE ACS in dB | 20 to 40** | 49.5 (own channel measurement BW: 1.23MHz adjacent channel measurement BW: 180kHz)

## Slide 9: Simulation Assumption
 | NB-IoT standalone | CDMA2000 1x
BS noise figure in dB | 5 | 5
UE noise figure in dB | 9 | 9
BS-UE path-loss model | TR36.942 macro urban | TR36.942 macro urban
Standard deviation of BS-UE log-normal shadow fading in dB | 10 | 10
Shadowing correlation | Inter-cell 0.5 intra-cell 1 | Inter-cell 0.5 intra-cell 1
Evaluation metrics | SINR vs ACS (as victim) | Capacity vs NB-IoT ACLR (as victim). For DL, capacity is the number of satisfied users. For UL, capacity is the number of users when 5.5dB noise rise is reached
Carrier separation*** | 1.1MHz to CDMA(central frequency separation) | 1.1MHz to NB-IoT(central frequency separation)
*DL overhead channel resource consumption, including pilot, paging and sync overhead.
**Similar to coexistence study in TR36.802, NB-IoT ACLR and ACS are defined for its own bandwidth size.
*** Other carrier separation options are not excluded.