## Slide 1: Way forward on BS Beamforming Model for the ITU WP5D coexistence simulations
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #80 R4-167127
Gothenburg, Sweden, 22 – 26 August, 2016

## Slide 2: Background: RAN1 Agreements on BS antenna modelling
Mg
Ng

## Slide 3: Background: RAN1 Agreements on BS antenna modelling
  At 30GHz:
    Dense urban and Urban macro:
      Baseline: (M,N,P,Mg,Ng) = (4,8,2,2,2). (dV,dH) = (0.5, 0.5)λ. (dg,V,dg,H) = (2.0, 4.0)λ.
      Note that companies are also encouraged to investigate a larger panel spacing, e.g. (dg,V,dg,H) = (4,8) λ
    Indoor hotspot:
      FFS
  At 70GHz:
    Dense urban:
      Baseline: (M,N,P,Mg,Ng) = (8,16,2,2,2). (dV,dH) = (0.5, 0.5)λ. (dg,V,dg,H) = (4.0, 8.0) λ.
      Note that companies are also encouraged to investigate a larger panel spacing, e.g. (dg,V,dg,H) = (8,16) λ
    Indoor hotspot:
      FFS

## Slide 4: WF
  At 30GHz:
    Dense urban and Urban macro:
      Baseline: Only one panel is assumed, (NV,NH) = (8,16).
      (dV,dH) = (0.5, 0.5)λ.
      An additional 3dB gain is added to the total beamforming gain to account for the two polarization directions.
    Indoor hotspot:
      FFS
  At [45] & 70GHz:
    Dense urban:
      Baseline: Only one panel is assumed, (NV,NH) = (8,16). (dV,dH) = (0.5, 0.5)λ.
      An additional 3dB gain is added to the total beamforming gain to account for two polarization directions.
    Indoor hotspot:
      FFS

## Slide 5: WF
The number of beams per cell:
  There is one beam formed using all the antenna elements.
The number of supported UEs:
  Each beam is directed to one scheduled UE. So there are 1 scheduled UEs
The weighting factors
  DFT (linear phase progression) based beamforming is assumed (details next slides)

## Slide 6: Composite Array radiation pattern

## Slide 7: Element pattern for antenna array model
3dB extra beamforming gain is added to account for the two polarization directions