## Slide 1: Way forward on NB-IoT UE demodulation requirements
NTT DOCOMO, Ericsson
3GPP TSG-RAN WG4 Meeting #80BIS
Ljubljana, Slovenia, 10-14, October, 2016
R4-168735

## Slide 2: NPDCCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 1% BLER in each case (Case 1&3 at SNR of -6dB, Case 2&4 at SNR of -12dB) from each contribution.
 | Case1 EPA5 2x1 low | Case2 ETU1 2x1 low | Case3 EPA5 1x1 | Case4 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [64] | [512] | [128] | [512, 1024]
Ericsson[R4-168208] | 128 | 512/1024 | 128 | 1024
Intel[R4-167243] | 128 | 768 | 128 | 1024
CATT[R4-167506] | 128 | 768 | 128 | 1024
Huawei[R4-167568] | 64 | 512 | 128 | 1024
Qualcomm[R4-168040] | TBD | TBD | TBD | TBD
ZTE[R4-168157] | 64 | 512 | 128 | 512
Nokia[R4-168368] | 128 | 512 | TBD | TBD
Samsung[R4-168148] | TBD | TBD | TBD | TBD
Agreement |  |  |  | 

## Slide 3: NPDSCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 70% of Max throughput around the targeted SNR.
 | Case2 EPA5 2x1 low | Case3 ETU1 2x1 low | Case4 EPA5 2x1 low | Case5 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [16] | [192, 128, 256] | [32] | [192, 128, 256]
Intel[R4-167244] | 32 | 256 | TBD | 192
CATT[R4-167507] | 32 | 256 | 64 | TBD
Huawei[R4-167569] | 16 | 256 | 32 | 256
Qualcomm[R4-168041] | 16 | 128 | 32 | 128
ZTE[R4-168158] | 16 | 128 | 32 | 128
Ericsson[R4-168209] | 32 | 256 | 32 | 192
Nokia[R4-168367] | 16/32 | 256/384 | 32 | 192/256
Samsung[R4-168148] | TBD | TBD | TBD | TBD
Agreement |  |  |  | 

## Slide 4: Agreement
TBD