## Slide 1: WF on simulation parameters for urban macro and TPC model
DOCOMO, Qualcomm
3GPP TSG-RAN WG4 Meeting #80bis R4-168795
2016Ljubljana, Slovenia, 10 – 14 October, 2016

## Slide 2: Back ground
InRAN4#80bis meeting, it is observed that many UEs are in outage coverage in case of urban macro with current simulation assumptions.
  For example from simulation results captured in R4-168466, 10~15% DL UEs will in outage coverage. In UL case, more UEs than DL will be in outage coverage.
Thus we may need to reconsider simulation assumptions for urban macro, which have impact on SINR such as IDS.

## Slide 3: Back ground: CDF of SINR (preliminary results)
Gamma=1
UL Allocation | CL-xile
50 | 94.0
100 | 91.0
200 | 88.0
Observation:
  With this simulation assumptions, ISD = 300, 50MHz, indoor 20%: about 5% UE in outage. (Note: 11dB is used as NF in this preliminary simulation results.)

## Slide 4: Back ground: UL Power (preliminary results)
Observation:
  With this simulation assumptions, ISD = 300, 50MHz, indoor 20%: 20% UE with Max power. (Note: 11dB is used as NF in this preliminary simulation results.)
Gamma=1
UL Allocation | CL-xile
50 | 94.0
100 | 91.0
200 | 88.0

## Slide 5: WF: simulation parameters for urban macro
Evaluate following two cases for urban macro UL and compare both results in Nov. meeting.
  Case 1: agreement in the last meeting
    ISD = 500m
    Transmission BW = 200MHz
    Indoor ratio = 80%
  Case 2:
    ISD = 300m
    Transmission BW = 20MHz
    Indoor ratio = 20%
  If we find any issue, then we can revisit parameters
  Other cases are not precluded in addition to Case 1 and 2.

## Slide 6: WF: TPC model
In order to start simulation campaign, following TPC model are assumed
  CL-xile = 88 + 10*log10(200/X)
    X: UL transmission BW
  Gamma = 1
  Note: we need discuss KPI based on simulation results.