## Slide 1: WF on inter-cell interference model and reference receiver for BS IC
China Telecom
3GPP TSG-RAN WG4 Meeting #81
Reno, Nevada, USA, 14 - 18 November, 2016
R4-1609049

## Slide 2: Background: agreements in RAN4 #80bis
Interference type:
  Intra-cell inter-user interference
  Further discuss on whether to model inter-cell interference in the link level evaluation
Reference Receiver
  Option 1: CWIC
    CWIC is used to mitigate uplink intra-cell inter-user interference
    IC iteration may or may not be implemented to further improve the receiver performance
    the Rel-13 BS MMSE-IRC receiver can be applied simultaneously for inter-cell interference suppression while CWIC receiver is used for intra-cell interference cancellation, if inter-cell interference are to be modelled
  Option 2: SLIC
  Down-selection to be made in the next meeting by taking complexity and performance into consideration
Baseline receiver for performance comparison
  MMSE receiver for intra-cell interference scenario only
  Rel-13 BS MMSE-IRC for inter-cell interference suppression, if inter-cell interference are to be modelled

## Slide 3: WF
CW-IC receiver is used as the reference receiver for intra-cell inter-user interference mitigation.
Introduce two sets of simulation cases for BS IC:
  Set 1: Model explicit inter-cell interference with high interference level (i.e., DIP1 at 85%-tile of the DIP1 distribution)
  Set 2: No explicit inter-cell interference