## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei, China Telecom, Nokia, ZTE
WF on BS IC deployment scenarios and inter-cell interference model
R4-1610707

## Slide 2: Background
During RAN4#80bis meeting, WF R4-168976 about BS IC was approved. The following agreements were reached:
Deployment scenario:
  Homogeneous deployment with macro cell only
  Heterogeneous deployment with co-channel low power node(LPN) within the macro cell coverage
  Further discuss if both are to be investigated in the SI
The following are considered as baseline, if inter-cell interference are to be modeled. Other options are not precluded.
  Reuse DIP based interference statistical measurement for BS IC
  Reuse the DIP profiles from BS MMSE-IRC WI
  FFS number of inter-cell interference
  Interference level
    Option 1: cover two interference levels
      high interference level which corresponds to the DIP1 values at 85%-tile of the DIP1 distribution
      low interference levels, which corresponds to 15%-tile of the DIP1 distribution
        For low interference level, if the link performance difference between low interference and AWGN only is negligible, there is no need to model explicit inter-cell interference in the link evaluation.
    Option 2: other options are not precluded
  Produce randomly modulated 16QAM symbols in the inter-cell interfering PUSCH.
  The boundaries of allocated PRBs for targeting user and interference users are always aligned.

## Slide 3: Deployment scenarios
Deployment scenario:
  Scenario 1: Homogeneous deployment with macro cell only
  Scenario 2: Heterogeneous deployment with co-channel low power node (LPN) within the macro cell coverage

## Slide 4: Inter-cell Interference Model
Introduce two sets for inter-cell interference:
  Set 1: Model explicit inter-cell interference with high interference level in co-channel heterogeneous scenario
  Set 2: Model explicit inter-cell interference with low interference level in homogeneous scenario
Number of inter-cell interferers
  1 for 2Rx with high and low interference level
  {1, 2} for 4/8Rx with high interference level and down select in the next meeting
  1 for 4/8Rx with low interference level
Reuse DIP based interference statistical measurement for BS IC
  Note 1: intra-cell inter-user interference is not included in the DIP definition, and the DIP ratio is the ratio of the power of a given dominant inter-cell interferer over the total power of all inter-cell interferers along with the white noise.
  Note 2: The DIP ratio is exactly same as that for co-scheduled intra-cell UEs
Reuse the DIP profiles from Rel-13 BS IRC
  High interference level with DIP1 at 85%-tile of the DIP1 distribution in heterogeneous scenario: (DIP, DIP2) = (-0.43, -13.78) dB
  Low interference level with DIP1 at 15%-tile of the DIP1 distribution in homogeneous scenario: DIP1 = -5.45 dB
    Note: DIP1 is used if 1 inter-cell interference is modeled
Consider synchronous interference only