## Slide 1: WF on OTA Sensitivity
NEC, Huawei, Ericsson
3GPP TSG-RAN WG4 Meeting #81 R4-1610807
Reno, USA, 14-18 Nov, 2016

## Slide 2: Background
WF in [1] was agreed during RAN4#80bis:
  A minimum EIS for AAS should be calculated according to the following formula:
    Minimum EIS = Conducted reference sensitivity – D + L
      L is a loss factor accounting for antenna losses, cable losses, integration losses etc.
      Conducted ref sens is rel13 value
      D represents the estimated minimum antenna directivity of a non AAS BS within the range of angles of arrival (that is part of the OSDD declaration), calculated using one of the options below.
  Minimum EIS represents a threshold for minimum sensitivity performance. Basestations with sensitivity better than minimum EIS will pass the requirement
  Two options exist for setting D. One of these options should be decided and adopted for the specification.
    Base D on a formula applied to the declared OSDD.
    Make a table of possible D based on BS class, number of sectors and possibly some other factors
      Contents of the table could be derived using the formula
  L may be set based on BS class, sectors etc. or some other method
  The minimum EIS level may not be the same level as is used for setting a power level for the wanted signal for the blocking and RX IM requirements
  It is for further studies whether the reference levels for the wanted signal in the blocking and RX IM requirements will be based on the minimum EIS
OTA sensitivity was discussed further during this meeting and the proposals in related contributions [2-5] were considered.

## Slide 3: Way Forward on OTA Sensitivity
The following is agreed
  For the purposes of setting minimum OTA sensitivity, the coverage pattern of a non-AAS with a similar coverage pattern to the AAS is assumed
  Minimum EIS requirements is calculated from the refined formula in [1] as indicated below
    Minimum EIS = Conducted reference sensitivity – D + L + Off-peak Margin
      L is a loss factor accounting for antenna losses, distribution losses, integration losses etc.
      Conducted reference sensitivity is rel13 value
      D represents the estimated antenna directivity of a non AAS BS which has a beam pattern related to the AAS BS range of angles of arrival (that is part of the OSDD declaration)
      Off-peak Margin is to allow coverage for the declared RoAoA other than just in the peak direction, using the same estimated antenna pattern used to derive D.

## Slide 4: Open Issues on OTA Sensitivity
The non-AAS antenna beam pattern which directivity D shall be applied in the agreed formula in the previous slide is still open.
Companies are encouraged to submit proposals for the next meeting addressing the following related open issues:
    Should the non-AAS beam pattern used to derive D be linked to the RoAoA declarations.
    What parameters bound the choice of non-AAS beam pattern, i.e. 3dB beam width, 10dB beam width or other…..
    The translation of equivalent non-AAS beam pattern to D to be done by either table or equation (e.g. Elliott formula).
    If the declared RoAoA concept needs to be updated, e.g. define the difference in EIS in dB between reference direction and edge of the RoAoA.
    Whether the Loss factor L in the min EIS formula is dependent on BS class or not and what value should it be.

## Slide 5: References
R4-168874, WF on OTA sensitivity, Ericsson, Nokia, NEC
R4-1609851, On finding a minimum requirement level for OTA sensitivity, Ericsson
R4-1610363, OTA Receiver Sensitivity for eAAS, NEC
R4-1610388, Estimating antenna gain using 3dB beam width, Huawei
R4-1610389 Further discussion on Minimum EIS, Huawei