## Slide 1: Discussion on V2X RRM requirement
LG Electronics
3GPP TSG-RAN WG4 Meeting #82 R4-1700852
Athens, Greece, 13 - 17 Feb, 2017
Agenda Item: 7.20.4

## Slide 2: Background
  Agreed WID in RP-162519
  Following prioritization shall be considered:
    Specify the following scenarios with first priority.
    Band 47 + Band 47 (Contiguous concurrent operation),
    Band 47 + Band X (Uu for V2X service),
    Band 47 + Band Y (Uu for non-V2X service)
      Band X or Band Y is licensed band such as Band 3,7,8,39,41
  Agreed WF In R4-168694
  The RRM requirements will be defined at least for V-UE.
  Existing RF reference for inter-band CA
  Separate RF chain
E‑UTRA Operating Band | Uplink (UL) operating band BS receive UE transmit |  |  | Downlink (DL) operating band BS transmit UE receive |  |  | Duplex Mode
 | FUL_low – FUL_high |  |  | FDL_low – FDL_high |  |  | 
3 | 1710 MHz | – | 1785 MHz | 1805 MHz | – | 1880 MHz | FDD
7 | 2500 MHz | – | 2570 MHz | 2620 MHz | – | 2690 MHz | FDD
8 | 880 MHz | – | 915 MHz | 925 MHz | – | 960 MHz | FDD
39 | 1880 MHz | – | 1920 MHz | 1880 MHz | – | 1920 MHz | TDD
41 | 2496 MHz |  | 2690 MHz | 2496 MHz |  | 2690 MHz | TDD

## Slide 3: General for V2X RRM requirement
  Proposal
  Rel-14 V2X RRM requirements are specified based on first priority of MCC operation in RF agreements.
    Band47+BandX/Y
      It is assumed that UL TX and SL TX use separate TX chains
  A shared carrier on V2X operation is deprioritized.
  A shared RF on V2X operation is deprioritized.

## Slide 4: UE Tx timing reference
  SCC with dedicated carrier(w/o cell)
  GNSS or SyncRef UE
  MCC with dedicated carrier
  GNSS or SyncRef UE for OoC on serving cell
  GNSS or eNB for InC on serving cell

## Slide 5: UE Tx timing requirement
  NTA offset(Ts)
  Proposal : Rel-14 V2X UE Tx timing requirements are specified based on the above scenarios.
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | 0 | N/A
GNSS | 0 | 0 | 0
SyncRef UE | 0 | N/A | 0

## Slide 6: Interruption
Background: RAN1 definition of cases
  Case 1: UL TX and SL TX use separate TX chains and separate power budget
  Case 2: UL TX and SL TX use separate TX chains but sharing power budget
  Case 3: UL TX and SL TX share TX chains and power budget
Background: RAN1 working assumption
  When UL TX overlaps in time domain with SL TX in different carrier frequency,
    The UE may drop UL TX or reduce UL TX power if the PPPP of SL packet is above a (pre)configured PPPP threshold, otherwise the UE may drop SL TX or reduce SL TX power.
  Note that UL TX power is always prioritized if PPPP threshold is set to the highest value.
Background: RAN4 agreement
  V-UE interruptions requirement WAN and PC5 MCC operation
    Case 1: No interruptions
    Case 2: FFS
    Case 3: Interruptions may happen
    Interruptions may happen when SL has higher priority than UL. Priority definition is FFS.
  WAN and PC5 shared carrier operation
    There is interruption when SL has higher priority than UL
  FFS on whether to capture interruption requirements in RAN4 specs

## Slide 7: Interruption
V-UE requirement on WAN interruptions
  SCC with shared carrier
    Be deprioritized in Rel-14 V2X even though there is interruption when SL has higher priority than UL
  SCC with dedicated carrier
    No interruption
  MCC with dedicated carrier
    Case 1: No interruptions
    Case 2:
      InC of BandX/BandY : Interruptions may happen when UL TX overlaps in time domain with SL TX in different carrier frequency if the PPPP of SL packet is above a (pre)configured PPPP threshold. However, there is no need to define duplicated WAN interruption requirements in RAN4.
      OoC of BandX/BandY : No interruptions
    Case 3:
      InC of BandX/BandY : Interruptions may happen when UL TX overlaps in time domain with SL TX in different carrier frequency if the PPPP of SL packet is above a (pre)configured PPPP threshold. However, it is deprioritized regarding existing dedicated inter-band RF chain.
      OoC of BandX/BandY : No interruptions

## Slide 8: Interruption
  WAN/GNSS timing misalignment
  Time misalignment b.t.w WAN/GNSS can be solved by DFN offset.
  However, if time misalignment still exists after DFN offset is applied in UE side
    SCC with shared carrier
      Be deprioritized in Rel-14 V2X
    SCC with dedicated carrier
      No interruption
    MCC with dedicated carrier
      Case 1: No interruption independent of time misalignment
      Case 2: No interruption independent of time misalignment
      Case 3: It is deprioritized regarding existing dedicated inter-band RF chain. And frequency retunning is independent of time misalignment.

## Slide 9: Interruption
  Synchronous source change to/from GNSS
  eNBGNSS or GNSSeNB(In-coverage for BX/BY)
  Timing error no change : 12Ts  12Ts
  Frequency error no change : 0.1ppm  0.1ppm
  Frequency retunning is not necessary for synchronous source change
Other cases in OoC
  No nterruption
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | eNBGNSS | N/A
GNSS | GNSSSyncRef UE | GNSSeNB | GNSSSyncRef UE
SyncRef UE | SyncRef UEGNSS | N/A | SyncRef UEGNSS

## Slide 10: Interruption
Requirements
  Proposal :
  Specify 1 subframe WAN interruptions due to V2X (re)configuration.
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | Define as below | N/A
GNSS | No interruption | Define as below | No interruption
SyncRef UE | No interruption | N/A | No interruption

## Slide 11: Initiation/cease of SLSS requirements
Requirements
  Proposal : Specify initiation/cease of SLSS requirements based on the above table.
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | Reuse Rel-12/13 in-coverage ProSe requirements | N/A
GNSS | N/A | Reuse Rel-12/13 in-coverage ProSe requirements | N/A
SyncRef UE | -Reuse D2D measurement accuracy - Measurement period = 320ms - Evaluation period = 640ms | N/A | -Reuse D2D measurement accuracy - Measurement period = 320ms - Evaluation period = 640ms

## Slide 12: Selection/Reselection of V2X Sync.Ref.
Requirements to SyncRef UE
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | N/A | N/A
GNSS | A | N/A | A
SyncRef UE | A | N/A | A

## Slide 13: Selection/Reselection of V2X Sync.Ref.
Requirements to SyncRef UE
Proposal :
  From SyncRef UE
    SCH Es/Iot ≥ [-4] dB
    Tdetect,SyncRef UE = [1.6]seconds
    Drop rate
      maximum [50]% of its SLSS(based on 5 samples of SLSS during Tdetect,SyncRef UE)
  From GNSS
    SCH Es/Iot ≥ [-4] dB
    Tdetect,SyncRef UE = [1.6]seconds
    Drop rate
      If GNSS is reliable and highest priority, no drop
      otherwise, maximum [50]% of its SLSS(based on 5 samples of SLSS during Tdetect,SyncRef UE)
  UE measurement capability of performing S-RSRP
    V-UE : [4] identified V2X SyncRef UE

## Slide 14: Selection/Reselection of V2X Sync.Ref.
Requirements to GNSS
  Proposal : Not define GNSS selection time based on tele-CC agreement
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | A | N/A
GNSS | N/A | N/A | N/A
SyncRef UE | A | N/A | A

## Slide 15: Selection/Reselection of V2X Sync.Ref.
Requirements to eNB
  Proposal : Not define eNB selection time as D2D
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | N/A | N/A
GNSS | N/A | A | N/A
SyncRef UE | N/A | N/A | N/A

## Slide 16: Selection/Reselection of V2X Sync.Ref.
  GNSS synchronization source reselection evaluation period
  eNB/SyncRefUEGNSS
    Tevaluate,GNSS,reliable does not need to be specified regarding the agreement of tele-CC that GNSS selection time is not defined.
  GNSSeNB/SyncRefUE
    Tevaluate,GNSS,unreliable does not need to be specified because that UE can sustain timing error of 12Ts for a few minutes.
  Proposal : Not specify GNSS synchronization source reselection evaluation period.

## Slide 17: Cell detection requirements in OOC
Requirements
  Proposal : Specify cell detection requirements in OOC based on the above table.
Timing Reference | SCC on dedicated carrier (B47) | MCC on dedicated carrier(B47+BX/BY) | 
 | OoC(B47) | OoC(B47) | 
 |  | InC(BX/BY) | OoC(BX/BY)
eNB | N/A | N/A | N/A
GNSS | N/A | N/A | Tbasic_identify_OoC_V2X = 0.8 seconds
SyncRef UE | N/A | N/A | Tbasic_identify_OoC_V2X = 0.8 seconds

## Slide 18: Autonomous Resource (re)selection
Proposal :
  Requirements
    The UE physical layer shall be capable of performing the PSSCH-RSRP measurements and the S-RSSI measurements on the carrier operating V2X sidelink communication for determining the subset of resources to be excluded in PSSCH resource selection in sidelink transmission mode 4.
    One shot measurement
  PSSCH-RSRP measurement accuracy
    Absolute accuracy: ± [5] dB at Es/Iot [-3]dB
    Relative accuracy: ± [2.5] dB at Es/Iot [0]dB
  S-RSSI measurement accuracy
    Reuse RSSI measurement accuracy in LAA

## Slide 19: Congestion control
Proposal
  Requirements
    The UE shall be capable of estimating the channel busy ratio on the carrier operating V2X sidelink communication, based on S-RSSI samples provided by the physical layer.
    Measurement period = 100ms.
  CBR measurement accuracy
    S-RSSI at the UE receiver meets the following condition with respect to the configured ThresS-RSSI_CBR :
      S-RSSI at the UE receiver is above ThresS-RSSI_CBR + ,
      : applicable S-RSSI measurement accuracy value from the S-RSSI measurement accuracy requirements