## Slide 1: 3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Ericsson
Simulation assumption for multiple-link V2V receiption
R4-1702315

## Slide 2: Background
In this contribution, simulation assumption are provided for companies to evaluate the mulitple-link V2V receiption

## Slide 3: WF on the simulation assumption
Companies are encouraged to provide analysis based on this simulation assumption for the discussion of multiple link receiption.
In the model, the numer of modelled UEs:
  Option 1: 2
  Option 2: more than 2 (e.g, 15 or 30)

## Slide 4: Simulation assumption for two-link performance evaluation
Parameters |  | Valuess
Bandwidth |  | 10 MHz
V2V TX UE #2k | Resource allocation for PSSCH | Option 1: 5 PRB Option 2: 15 PRB
 | MCS | 16QAM 1/2, 2 TTI
 | Propagation condition | EVA[180 or 1000]
 | Transmit Time offset vs GNSS | -12 Ts
 | Frequency offset vs GNSS | +600 Hz
V2V TX UE #2k+1 | Resource allocation for PSSCH | Option 1: 5 PRB Option 2: 15 PRB
 | MCS | QPSK 1/3; 1 TTI
 | Propagation condition | ETU[1000 or 1500]
 | Transmit Time offset vs synch. | 12 Ts
 | Frequency offset vs GNSS | -600 Hz
Synchronization |  | GNSS or GNSS-equivalent
Note: The resource allocation of the first link is put in one edge of the bandwidth and the resource allocation of the second is put in the other edge of the bandwidth, it is subjected to change based on the discussion. |  | 

## Slide 5: Information
Companies are encouraged to have the following modeling methods in the simulation
  Explicitly model joint decoding of control and data in each link.
  Explicitly model decoding of the two link under the given channel.
Simulation results are aligned after the simulation result for single link test are aligned.