## Slide 1: WF on NR subcarrier spacing and Channel bandwidth
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13th – 17th February, 2017
R4-1702096
Agenda item: 10.2
Document for: Approval

## Slide 2: Back ground (SCS)
Following SCSs are proposed in this meeting
  For sub 6GHz, 15k, 30k, and 60k are included in all companies’ proposals
  For above 6GHz, 60k, 120k and 240k are included in most companies’ proposals
R4-170xxxx | 
Qualcomm (1797) | 
Nokia (0724) | 
Ericsson (1166) | 
Huawei (1314) | 
Intel (2031) | 
2GHz
2.5GHz
3.5GHz
6GHz
24GHz
43.5GHz
52.3GHz
15k, 30k, 60k
15k, 30k, 60k
15k, 30k, 60k
15k
30k
60k
120k
240k
120k, 240k
60k, 120k, 240k, 480k (*)
* These are a set of possibilities, not proposals. Final set will depend on evaluations 480k should not be precluded at this stage.
15k, 30k, 60k
60k, 120k

## Slide 3: Back ground (CBW)
Following maximum CBWs are proposed in this meeting
R4-170xxxx | 
Qualcomm (1797) | 
Nokia (0724) | 
Samsung (1075) | 
MediaTek (1824) | 
Intel (2031) | 
2GHz
2.5GHz
3.5GHz
6GHz
24GHz
43.5GHz
52.3GHz
100M
200M
200M
20M
50M
100M
200M
400M
400M
1G
1G
100M
400M

## Slide 4: Back ground
RAN1 made following agreement in this meeting.

## Slide 5: WF on SCS
For sub 6GHz
  15kHz, 30kHz, and 60kHz are feasible SCS
For above 6GHz
  RAN4 has not yet reached a decision on which SCS are feasible
  60kHz, 120kHz and 240kHz are potential candidates for SCS
    Feasibility of 480kHz is FFS
  Evaluation of feasible SCS should be made based on the phase noise model(s), CBW, FFT size, service to support etc.
  Which of the above mentioned SCSs are supported for NR bands will be discussed in WI phase.
    SCSs mentioned above are not applicable to all bands
Note: RAN4 discussion is for common or dedicated data channel and is not applicable for special channel such as PRACH or sync channel, which is dependent on RAN1 progress.

## Slide 6: WF on CBW
For sub 6GHz
  Maximum CBW would be considered in range of 100MHz~200MHz
  Maximum CBW will be further studied in range of 100MHz ~ 200MHz.
For above 6GHz
  Maximum CBW would be considered in range of 200MHz~1GHz
  Maximum CBW will be further studied in range of 100MHz ~ 1GHz.
Maximum CBW to be supported for NR bands will be discussed in WI phase
      Maximum CBW mentioned above may be not applicable to all bands, e.g. for low frequency bands
      In case operator has spectrum higher than the maximum CBW, CA can be used to utilize whole spectrum
Subsets of CBW will be discussed in WI phase.

## Slide 7: WF FFT size
For the maximum FFT size
  4096 FFT size is feasible
  feasibility of 8192 FFT size is FFS
Note: there is no mandate on UE and BS implementation with respect to FFT size.