## Slide 1: WF on Enhanced CRS-IM Network Assistance
Intel Corporation, LGE, Ericsson, ….
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Agenda Item: 7.31
R4-1702452

## Slide 2: Background (1)
To mitigate the interference for the CRS from the neighbouring cell UE needs information on the following neighbouring cell parameters:
  Physical Cell ID: this information is required to derive CRS sequence and CRS RE mapping
  Number of CRS APs: together with Cell ID this information allows to derive CRS RE mapping
  MBSFN subframe configuration: this information allows UE to adjust behaviour for the MBSFN subframes, where CRS may be present in the control region only.

## Slide 3: Background (2)
For Rel-13 CRS-IM eNB is expected to provide UE CRS Assistance information using RRC signalling (CRS-AssistanceInfo-r13 IE)
  CRS assistance RRC signalling may result in non-marginal overhead in case of dense multi-carrier deployments.
  The CRS Assistance parameters can be similar for multiple different cells in one network
  MBSFN subframe configurations may not be commonly used in all networks
UEs may be capable of blind detection of neighboring cell PCID and number of CRS APs. Detection of neighboring cell MBSFN subframe configuration may impose higher complexity and may be unreliable under certain scenarios.

## Slide 4: Way Forward
Investigate possible solutions to reduce the CRS assistance signalling overhead for CRS-IM
Candidate solutions
  Solution #1:
    Introduce optional UE capability of CRS assistance information blind detection of PCID and Number of CRS APs.
      No MBSFN subframe configuration blind detection is used
      Companies are encouraged to provide analysis on reliability of blind detection of Number of CRS APs
    eNBs provide CRS Assistance to the blind detection capable UEs only when
      Option A: neighboring cell use MBSFN subframes
      Option B: neighboring cells MBSFN configuration is different from the serving cell
  Solution #2:
    eNBs provide reduced size CRS assistance information for the cells using same configuration as the serving cell
  Other solutions are not precluded
If no further solution is to be agreed the eNBs provide the same CRS-assistant info as legacy Rel-13 CRS-IM.