## Slide 1: WF on CA 256QAM and 4 layer MIMO demodulation test
Qualcomm
3GPP TSG-RAN WG4 Meeting #82bis Spokane, U.S., 3 - 7 April 2017
R4-1704270

## Slide 2: Background
RAN4 specified following tests to verify 256QAM demodulation test
  TM4 rank 2 PDSCH demodulation test for 2/4 Rx UE
  TM9 rank 1 PDSCH demodulation test for 2 Rx UE
  SDR test for 2/4 layer MIMO and 256QAM for 2/4 Rx UE
RAN4 specified following tests to verify 4 layer demodulation test
  TM4 rank 4 PDSCH demodulation test for 4 Rx UE
  TM9 rank 4 PDSCH demodulation test for 4 Rx UE
  SDR test for 4 layer MIMO 4 Rx UE
In Rel-14 4 Rx CA WI, it was proposed to specify new CA 256QAM and 4 layer PDSCH demodulation test in fading channel

## Slide 3: Background
Option 1
  Existing 256QAM and 4 layer demodulation test cannot verify UE’s 256QAM and 4 layer demodulation performance in fading channel
    UE can choose to implement full complexity receiver in single carrier mode but might implement simplified receiver in CA mode
    UE with full complexity receiver can fulfill 256QAM and 4 layer demodulation test in fading channel
    Simplified UE implementation can fulfill SDR test requirement in CA but cannot fulfill fading channel requirement in CA
  RAN4 should specify new CA 256QAM and 4 layer PDSCH demodulation test in fading channel
Opinion 2
  Existing 256QAM and 4 layer demodulation test can guarantee UE’s 256QAM and 4 layer demodulation performance in fading channel
  RAN4 does not need to specify new CA 256QAM and 4 layer PDSCH demodulation test in fading channel

## Slide 4: Way Forward
Verify need for CA demodulation test for 256QAM in fading channel by example UE implementation with simplified receiver
Proponent of new tests proposes example UE implementation with simplified receiver
Evaluate demodulation performance of example UE in following tests
  64QAM/16QAM CA demodulation test in fading channel
  256QAM SDR test
  256QAM PDSCH demodulation test in fading channel
Confirm need for CA demodulation test for 256QAM in fading channel if
  Example UE fulfills 64QAM/16QAM CA demodulation test in fading channel
  Example UE fulfills 256QAM SDR test
  Example UE cannot fulfill 256QAM PDSCH demodulation test in fading channel

## Slide 5: Way Forward
Verify need for CA demodulation test for 4 layer MIMO in fading channel by example UE implementation with simplified receiver
Proponent of new tests proposes example UE implementation with simplified receiver
Evaluate demodulation performance of example UE following tests
  64QAM/16QAM CA demodulation test in fading channel
  4 layer MIMO SDR test
  4 layer MIMO PDSCH demodulation test in fading channel
Confirm need for CA demodulation test for 4 layer MIMO in fading channel if
  Example UE fulfills 64QAM/16QAM CA demodulation test in fading channel
  Example UE fulfills 4 layer MIMO SDR test
  Example UE cannot fulfill 4 layer MIMO PDSCH demodulation test in fading channel