## Slide 1: Way forward on emissions scaling
Agenda Item: 9.12.2.6
Document for: Approval
Source: Nokia, Alcatel-Lucent Shanghai Bell, Huawei
3GPP TSG-RAN WG4 #82bis R4-1704325
Spokane, WA, USA, 3rd – 7th April 2017

## Slide 2: Background
During the AAS evening ad hoc meeting, 5 contributions [1]-[5] on OTA emissions scaling were discussed
No consensus was reached on whether a fixed scaling factor (8 for E-UTRA or 4 for UTRA) or a similar scaling factor as the hybrid case should be adopted
What has already been agreed:
  Hybrid unwanted emissions requirements use the same scaling factor as the existing Rel-13 conducted AAS BS requirements

## Slide 3: Agreements (1/2)
Based on the discussion during online and offline meetings, the following is proposed:
Proposal:
  In Section 4.4, TR 37.843, the description of the OTA AAS BS is modified from
    “Figure 4.4-2 shows a general architecture of an OTA AAS BS radio architecture, where M is the total number of transceiver units”
    to
    “Figure 4.4-2 shows a general architecture of an OTA AAS BS radio architecture, where M is the total number of transceiver units and M ≥ 8 (E-UTRA) or 4 (UTRA)”
  Justification for OTA AAS BS for having more than 8 (E-UTRA) or 4 (UTRA) TRX will be captured in TR

## Slide 4: Agreements (2/2)
  The restriction highlighted on slide 3 proposal 1 will be captured in TS 37.105 (Section 4), TR 37.843 (Section 4), TS 37.145, TS 37.114
  A note to state the background of the maximum scaling factor 8 and RAN4 can reconsider this maximum scaling when number of layers/streams are updated. From TR 37.842, Section 8.2.6:
    “The fixed scaling factor of 8 is based on the maximum number of layers/streams specified in release 12 of 3GPP specifications. The scaling function may be further reconsidered for future releases if the maximum number of layers/streams supported is changed.”

## Slide 5: References
[1] R4-1703039, Discussion on scaling factor for OTA AAS BS, CATT
[2] R4-1703382, Scaling for OTA Unwanted Emissions Requirement, Ericsson
[3] R4-1703483, Proposal and view on emission scaling for eAAS, NEC
[4] R4-1703906, Discussion - OTA emissions scaling factor, Huawei
[5] R4-1703998, Definitions of OTA emissions scaling terminology, Nokia, Alcatel-Lucent Shanghai Bell