## Slide 1: Motivation for new WI on Performance requirements of interference cancellation receiver for LTE BS
China Telecom
May, 2017
R4-1704563

## Slide 2: Motivation for BS IC receiver
LTE UL is interference limited in typical networks, and co-channel interference has substantial impact on UL cell average and cell edge throughput.
Base station (BS) interference cancellation (IC) receiver can be utilized to mitigate the co-channel intra-cell inter-user interference.
BS IC receiver
Decoding of One UE’s signal
Re-construction of the UE’s signal
Decoding of one other UE’s signal
  Full knowledge of interference parameters is available at the target cell, and code-word level IC receiver is feasible.
  The utilization of BS IC receiver is transparent to the users, and the performance gain of BS IC receiver can also be enjoyed by legacy users.

## Slide 3: Summary of BS IC SI
A SI “Study on interference cancellation receiver for LTE BS” was approved at RAN #73 in September 2016 [1], and is to be complete at RAN #76 in June 2017.
The SI output is documented in TR 36.766 [2], and summarized as follows:
Scenario
  Homogeneous and heterogeneous network scenarios are introduced with considerations of interference among data channels (PUSCH).
Receiver
Evaluation
  Link-level simulations are performed to evaluate the performance gain of reference receiver over baseline receiver.
  22 simulation cases with different Rx antenna numbers, propagation conditions, MCS levels and inter-cell interference levels are evaluated.
  It is concluded that, BS IC receiver can achieve significant performance gain over baseline receiver.
  For the reference receiver, CW-IC receiver is used for intra-cell inter-user interference mitigation.
  In multi-cell scenario, for both baseline and reference receivers, inter-cell interference suppression with MMSE-IRC is implemented.

## Slide 4: Proposal and scope
Proposal
  Start a RAN4-led WI to specify new demodulation performance requirements of BS IC receiver under typical deployment scenarios and with practical receiver implementation.
Scope
  LTE BS CW-IC receiver shall be assumed as the reference receiver structure for specifying the requirements.
    CW-IC receiver is used for intra-cell inter-user interference mitigation.
    In multi-cell scenario, inter-cell interference suppression with MMSE-IRC is implemented in the reference receiver.
  For PUSCH, specify the enhanced demodulation performance requirements for verification of BS receiver’s ability on intra-cell inter-user IC.
    Introduce the test case set as recommended in TR 36.766.
    Use the test metric as recommended in TR 36.766.
  Specify the enhanced conformance test requirements.

## Slide 5: References
[1] 3GPP RP-161485, “New SI: Study on interference cancellation receiver for LTE BSNew SI: Study on interference cancellation receiver for LTE BS”, RAN #73, Sep 2016.
[2] 3GPP R4-17xxxxx, “TR 36.766: Study on interference cancellation receiver for LTE BS ”, RAN4 #83, May 2017.

## Slide 6
Thanks!

## Slide 7: Annex: IC performance gain concluded in SI (1/3)
For scenarios with 2Rx BS and equal SNR for intra-cell UEs:
  The average IC gain for cases with EPA5 serving channel and high interference level is [3.0 ~ 3.5] dB from per UE perspective (case E1-a1, E1-a2, E1-c).
  The average IC gain for cases with EVA70 serving channel and low interference level is [1.7 ~ 1.8] dB from per UE perspective (case E1-b1, E1-b2).
  There is no obvious difference in terms of IC gain between UE1 and UE2.
For scenarios with 4Rx BS and equal SNR for intra-cell UEs:
  The average IC gain for cases with EPA5 serving channel and high interference level is [3.9 ~ 5.5 dB from per UE perspective (case E2-a1, E2-a2).
  The average IC gain for cases with EVA70 serving channel and low interference level is [2.4 ~ 3.0 dB from per UE perspective (case E2-b1, E2-b2).
  There is no obvious difference in terms of IC gain among the 4 UEs.

## Slide 8: Annex: IC performance gain concluded in SI (2/3)
For scenarios with 2Rx BS and unequal SNR for intra-cell UEs (the SNR of UE1 is 3 dB lower than that of UE2):
  If all UEs use the same MCS
    The average IC gain for cases with EPA5 serving channel and high interference level is [5.2 ~ 5.7] dB and [1.5 ~ 1.7] dB for UE1 and UE2 respectively.
    The average IC gain for cases with EVA70 serving channel and low interference level is [3.5 ~ 4.0] dB and [0.5] dB for UE1 and UE2 respectively.
  If UEs with different SNR use different MCS
    When MCS 10 is used for UE1 and MCS 15 is used for UE2, with EPA5 serving channel and high interference level, the average IC gain is [2.6] and [3.6] dB for UE1 and UE2 respectively.
    When MCS 15 is used for UE1 and MCS 10 is used for UE2, with EPA5 serving channel and high interference level, the average IC gain is [7.8] and [0.2] dB for UE1 and UE2 respectively.

## Slide 9: Annex: IC performance gain concluded in SI (3/3)
For scenarios with 4Rx BS and unequal SNR for intra-cell UEs (the SNR of UE1/3 is 3 dB lower than that of UE2/4):
  If all UEs use the same MCS
    The average IC gain for cases with EPA5 serving channel and high interference level is [6.7 ~ 8.4] dB and [2.2 ~ 4.1] dB for UE1/3 and UE2/4 respectively.
    The average IC gain for cases with EVA70 serving channel and low interference level is [4.3 ~ 5. 6] dB and [1.5 ~ 2.1] dB for UE1/3 and UE2/4 respectively.
  If UEs with different SNR use different MCS
    When MCS 10 is used for UE1/3 and MCS 15 is used for UE2/4, with EPA5 serving channel and high interference level, the average IC gain is [4.6 ~ 4.8] and [5.7 ~6.0] dB for UE1/3 and UE2/4 respectively.
    When MCS 15 is used for UE1/3 and MCS 10 is used for UE2/4, with EPA5 serving channel and high interference level, the average IC gain is [11.1 ~ 11.2] dB and [2.3 ~ 2.5] dB for UE1/3 and UE2/4 respectively.