## Slide 1
3GPP TSG-RAN WG4 #84 R4-1707427 Berlin, Germany, 21 - 25 August, 2017
Agenda item: 7.9.2 - UE RF(36.101) [LTE_feMTC-Core]
Document for: Approval
Co-existence between B1 Cat.M2 UE and PHS in Japan
KDDI Corporation

## Slide 2: Background
CR for specifying Cat.M2 UE into TS36.101 was agreed in RAN4#83 and approved in RAN#76.
On the other hand, some of requirements have not been reached agreement in RAN4, for example, A-MPR for Band 1 (NS_05) is still “TBD”.
This contribution tries to show work plan for Cat. M2 NS_05.

## Slide 3: Discussion (1/3)
When NS_05 is indicated in the cell, below additional requirements shall apply.
Frequency band (MHz) | Channel bandwidth / Spectrum emission limit (dBm) |  |  |  | Measurement bandwidth | NOTE
 | 5MHz | 10MHz | 15MHz | 20MHz |  | 
1884.5 £ f £1915.7 | -41 | -41 | -41 | -41 | 300 KHz | 1
Table 6.6.3.3.1-1: Additional requirements (PHS)
What RAN4 should study is the worst case for each channel bandwidth.
From current version of the specification, at least RAN4 should study;
  15MHz CBW case @ Fc = 1932.5 MHz
  20MHz CBW case @ Fc = 1930 MHz
PHS
20M CBW worst case
Band 1 UL
15M CBW worst case
Operator B
Operator C
1884.5 1915.7 1920 1940 1960 1980
15M CBW@Fc = 1932.5MHz
20M CBW@Fc = 1930MHz
( * Physically, the worst case is @Fc = 1927.5 MHz but spectrum holder does not use such arrangement)

## Slide 4: Discussion (2/3)
For 20MHz@Fc=1930MHz, RAN4 should study as below;
20M CBW@Fc=1930MHz
PHS
GB
Narrow band Region
Case#1: Single RB (1RB) transmission
Case#2: Full RB (24RB) transmission
1884.5 1915.7 1920 1940
For Case#1, discussion point is whether IM3 reaches PHS or not.
 If it reaches, applying current A-MPR (= 11 dB) is reasonable.
For Case#2, RAN4 never simulates similar case (= Left most side of 5MHz CBW)

## Slide 5: Discussion (3/3)
For 15MHz@Fc=1932.5MHz, RAN4 should study as below;
15M CBW@Fc=1932.5MHz
PHS
GB
Narrow band Region
Case#3: Single RB (1RB) transmission
Case#4: Full RB (24RB) transmission
1884.5 1915.7 1920 1925 1940
For Case#3, IM3 will not reach PHS because frequency separation is enough.
 Applying current A-MPR (= 11 dB) is NOT necessary. New value is required.
For Case#4, frequency separation is enough as well. No A-MPR will be required (but should be confirmed by simulation results from vendors).

## Slide 6: Proposals
Simulation results for Case#1 ~ #4 from multiple companies should be submitted in RAN4#84-bis.
Considering this WI is for Rel. 14, CR for satisfying NS_05 requirements should be agreed in RAN4#85.