## Slide 1: WF on CRS muting for eFeMTC
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #84 R4-1708298
Berlin, Germany, 21th – 25th August, 2017
Agenda Item: 8.25.3.1

## Slide 2: Proposal:
Evaluate on how many warm-up subframes are required before
  UE initial transmission in a DRX or eDRX_CONN cycle
  PBCH/SI/Paging/PDSCH acquisition in connected DRX, eDRX_CONN cycle
  PBCH/SI/Paging/PDSCH acquisition in idle mode, eDRX_IDLE cycle
  Both CEModeA and CEModeB need to be considered.
The purpose of warm-up subframes are to acquire precise time and frequency tracking for demodulation or UL transmission
Companies are encouraged to provide CRS sampling rate and number of CRS needed for RSRP/RSRQ measurement and RLM for eMTC.

## Slide 3: Simulation assumptions
Parameter | Value
Sys BW | 10MHz
Duplex Mode | TDD
Channel | EPA5, ETU30
SNR | CEModeA: -6dB CEModeB: -15dB
Repetition of PBCH/PDSCH | Enabled
Antenna Configuration & Correlation | 2x1 low
Initial UE frequency and time error before wake up | To be indicated considering eDRX_idle, eDRX_CONN, DRX in connected mode and idle mode
Metrics | Number of warm up subframes to ensure 1. UE initial transmission timing error shall be less than or equal to Te 2. Successful PBCH/SI/Paging/PDSCH decode after wake up