## Slide 1: WF on spurious emissions limit for mm wave bands
R4-1708838
Ericsson, Qualcomm Incorporated, Skyworks, Huawei, Samsung, Nokia…

## Slide 2: Background
ITU-R has sent an LS to RAN4 to clarify
  Feasibility of achieving -30dBm spurious emissions limit
    If not, limit that would be feasible
  Feasibility to meet more stringent limits for specific bands

## Slide 3: Way Forward (1)
It is agreed that achieving -30dBm spurious emissions close to the carrier is not feasible considering factors such as PA efficiency, linearization feasibility, filtering, 2nd harmonic, image rejection etc.
  Concerns UE and BS.
-13dBm is assumed as the achievable baseline for mm wave spurious emissions at this stage, for both UE and BS
It is observed that UE emissions are not flat in the passive bands, this should be considered when performing simulation relating to the UE in the sharing study
The following are FFS
  What levels are achievable in the bands to which special limits apply, and suitable measurement bandwidths for these bands
  Feasibility of meeting -30dBm spurious emissions (or other value) with a (large) offset above and below the carrier/band

## Slide 4: Way Forward (2)
Based on the outcome of the analysis, the following option(s) might be considered as additional requirement(s) to protect specific bands (e.g. bands where passive services are operating):
  Define a different emission level in the protected band with larger measurement BW (e.g. 100MHz/200MHz). The value would be obtained by integrating an emission level tighter than -13dBm/MHz. The value to be adopted is this option is selected is FFS
  Define a tighter emission level in the passive bands and provide a number of exceptions. Emission level and number of exceptions to be adopted if this option is selected are FFS
  The solution for UE and BS may differ; e.g. exceptions, wider measurement bandwidth etc. may be a solution for the UE but a different solution may be needed for the BS
For NR channels in which OOB region overlaps with protected bands, SEM requirement can apply in the OOB domain.

## Slide 5: References
[1] R4-1707701, “Feasibility of improved spurious emissions in NR mmWave UE”, Skyworks Solutions Inc.
[2] R4-1708125, “On spurious emission limits for mm-wave bands”, Ericsson.
[3] R4-1708450, “General observations on UE emissions in mmW”, Qualcomm Incorporated.